MICHIGAN

DEPARTMENT OF TRANSPORTATION

SPECIAL PROVISION

FOR

LIGHTS ON TRAFFIC CONTROL DEVICES

C&T:BRZ                                                   1 of 2	                C&T:APPR:JKG:DBP:05-18-07

Replace the second sentence of Section 812.03.F.5.b, Channelizing Devices, on page 596 with the following.

Provide one Type D warning light on each plastic drum used during hours of darkness.

Delete the Section 812.03.I.6, Maintaining Lights, on page 605 of the Standard Specifications for Construction and replace with the following.

6. Maintaining Lights.  Position and maintain Type A, Type C and Type D lights to be visible on a clear night from a distance of 3000 feet.  Maintain Type B high intensity lights to be visible on a sunny day from a distance of 1000 feet when viewed without the sun directly on or behind the light.  Replace the power source when lights do not meet these requirements.  Provide and maintain Type C and Type D LED lights that meet or exceed all requirements in the MMUTCD.  Maintain the intensity requirement of 2 candela in the field.  This requirement does not preclude the Engineer from determining that a power source change is necessary.

Intermixing of different light styles or designs in a project will not be allowed.

All lights are required to work at the time of deployment to the roadway, and at all stage changes during the project.  During the project, inspect and maintain each light to ensure a minimum of 95 percent of the total working.  A maximum of 3 non-operational lights adjacent to each other is permitted at any time.

Delete the sentence in item 5 of Section 812.04.A.5, Damage Compensation, on page 616 of the Standard Specifications for Construction in its entirety, and replace with the following.

Replace damaged or non-functioning Type D lights at the Contractor’s expense.

Add the following paragraph at the beginning of section 812.04.C, Maintaining Lights on High Intensity Plastic Drums, and Type III High Intensity Barricades on page 617 of the Standard Specifications for Construction.

The Contractor is required to maintain all lights on plastic drums in working order at all times without direction from the Engineer.

Replace the first sentence of section 812.04.C, Maintaining Lights on High Intensity Plastic Drums, and Type III High Intensity Barricades on page 617 of the Standard Specifications for Construction with the following.

If notice is given by the Engineer that maintenance is necessary on more than ten percent of the Type C LED lights in service on Type III, high intensity barricades and these lights are not maintained according to subsection 812.03.I.6 within 72 hours, a five percent reduction in the unit price bid will be applied for Barricade, Type III, High Intensity, Lighted, Furn; Barricade, Type III, High Intensity, Lighted, Oper; Barricade, Type III, High Intensity, Double Sided, Lighted, Furn; and Barricade, Type III, High Intensity, Double Sided, Lighted, Oper.

Add the following to the end of Section 922.05.B, Warning Lights, on page 874 of the Standard Specifications for Construction.

4.  Type D – 360 degree steady burn warning light, yellow lens, battery operated.

The lens for the Type D lights on plastic drums shall be visible for 360 degrees.  The LED light source shall emit light equally for 360 degrees and be capable of sustaining constant brightness evenly distributed throughout the lens until no longer able to maintain the intensity requirements detailed in section 812.03.I.6.