For copies of this manual contact the MDOT Publications Office

Telephone: (517) 322-1676	Fax: (517) 322-1395

E-Mail: MDOT-Publications@Michigan.gov

Or visit our Web Site at

http://michigan.gov/mdot/0,4616,7-151-9622_11044---,00.html

The 2018 Minimum Acceptance Requirements for Material Approvals and Documentation Guide has been edited by the team of:

Tim Anderson, Bay Region

Mohammad Azam, Construction Field Services Division

Mike Cornacchia, Metro Region

Steve Hawker, University Region

Channing Page, University Region

Robert Smrek, Southwest Region

Michael Stoltz, Grand Region

Matthew Thomas, Bay Region

The information contained in the report was compiled exclusively for the use of the Michigan Department of Transportation.  Recommendations contained herein are based upon the research data obtained and the expertise of the researchers, and are not necessarily to be construed as Department policy.  No material contained herein is to be reproduced – wholly or in part – without the expressed permission of the Engineer of Construction Field Services.

DOCUMENTATION REQUIREMENTS FOR PROJECTS

This document is intended for use as a GUIDE to assist in project documentation of construction operations.  It is a working document and will be updated as required.  It is the responsibility of the managing office preparing the project record files to verify that the requirements are current.

FINAL ESTIMATE REVIEWS

The purpose of the Final Estimate Review is to determine whether the documentation is in substantial compliance with the plans, specifications and properly authorized contract modifications.  Refer to MDOT Construction WIKI 109.07.06.

When the Construction/Project Engineer has determined the final quantities of all pay items and has received all material documentation, the Region Construction Engineer should be notified that the project is ready for a final estimate review.  A review team will meet with the Construction/Project Engineer to review the project documentation.  The Construction/Project Engineer is to provide the review team with work space, read only access to the FieldManager files, all of the project files and access to personnel familiar with the project and file documentation.  All of the files shall be provided at one physical location.

The review team will evaluate the following questions:

●	Was the pay item measured according to specifications?

●	Were the source documents (pay items and testing) validated by signatures and dates?

●	Were the prescribed forms used?

●	Were the testing frequencies correct?

●	Were the materials listed on the signed Material Source List?

●	Were the materials approved per MDOT specifications?

●	Were the pay items and materials used and approved in FieldManager?

Particular attention will be focused on the proper use of FieldManager, FieldBook, and ProjectWise in the cross-referencing of pay items and source documents (IDRs, certifications, test reports, project file for numbers/descriptions/forms, etc.).    The correct use of FieldManager provides reviewers with good cross-references for finding the documentation in the files.

NOTES PAGE:

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

Aggregate:	A minimum of one satisfactory test per tester/per season (NHS Routes ONLY)

Concrete Field Testing:	A minimum of one satisfactory test, per tester/per season (NHS Routes ONLY)

Concrete Cylinder Strength Testing: 	A minimum of one satisfactory test, per tester/per season

Density:	A minimum of one satisfactory test per tester/per type/per season (NHS Routes ONLY)

HMA:	A minimum of one satisfactory test, per tester/ per type / per season (NHS Routes ONLY)

MDOT LET PROJECTS:

Aggregate, Concrete Field Testing, Density, and HMA testing must be performed by:

QA testing personnel must be CERTIFIED .

AGGREGATES:

One scale test per year if plant is stationary (if material is paid by the ton), per section 104.01.F of the Current Standard Specification.

BUY AMERICA:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

Construction Manual WIKI:

Refer to the Construction Manual for current and updated information.  MDOT Construction WIKI

MATERIAL SOURCE GUIDE:

Verify requirements from current edition of the guide at the time of letting. MDOT MSG

MATERIAL SOURCE LIST (FORM 501):

The completed 501 must be submitted in to ProjectWise by the contractor.

See the MDOT Construction WIKI section 105 for the requirements.

Qualified Products List (QPL):

a QPL material should be field verified by construction staff to the extent possible.

The Office Tech must verify that material listed on the Material Source List is from the QPL.

See the Material Source Guide.

TICKETS:

Immediate possession of tickets is required for items paid by ton (weight).

TABLE OF CONTENTS

PAY ITEM CODE(S)	PAY ITEM DESCRIPTION	PAGE NO.

2050001	Backfill, Swamp	1-2

2050010	Embankment, CIP	3-4

2050011	Embankment, LM	5-6

2050012	Embankment, Structure, CIP	7-8

2050016	Excavation, Earth	9

2050040	Subgrade Undercutting, Type I	10

2050041	Subgrade Undercutting, Type II	11-12

2050042	Subgrade Undercutting, Type III	13

2060002 	Backfill, Structure, CIP	14-15

2080025	Erosion Control, Silt Fence	16

3010002 &	Subbase, CIP

3010003	Subbase, LM	17-18

3020001 &	Aggregate Base

3020002 &	Aggregate Base, LM

3020008 - 3020030	Aggregate Base, __ inch	19-21

3030004 - 3030006	Open-Graded Dr Cse, __ inch	22-23

3050002	HMA Base Crushing And Shaping	24

3060005 - 3060006 &	Aggregate Surface Cse

3060010 - 3060016	Aggregate Surface Cse, __ inch	25-26

3070001 - 3070051 &	Approach Cl I; Cl II; and Cl III

3070101 - 3070162	Shoulder Cl I; Cl II; Cl III; and Cl IV	27-28

3080005	Geotextile, Separator

3080010	Geotextile, Stabilization

4010012 - 4010108	Culvert End Sections	29

4010131 - 4010698	Culverts	30-32

4020001 – 4021133	Sewer, Cl __, __ inch, Tr Det __	33-36

4030010 - 4030090	Dr Structure Cover, Type __ xx	37

4030200 – 4030271 	Dr. Structure,__ inch dia;

Dr Structure, Add Depth, __ inch dia, 8 Ft to 15 Ft;

Dr Structure, Add Depth, __ inch dia, Over 15 Ft	38-42

4040001 – 4040089 &	Underdrain,(Subgrade, Bank, Fdn., Subbase, Pipe, PDS and Edge of Pavt.)

4040091 – 4040099 	Underdrain Outlets	43-45

4040111 - 4040115	Underdrain, Outlet Ending, __ inch	46

5010025 - 5010806	HMA, __; HMA Approach	47-48

6020002 - 6020010 &	Conc Base Cse, Reinf, __ inch

6020015 - 6020023 &	Conc Base Cse, Nonreinf, __ inch

6020030 - 6020031 &	Conc, Grade __

6020050 - 6020062 &	Conc Pavt, Misc, Nonreinf, __ inch

6020070 - 6020082 &	Conc Pavt, Misc, Reinf, __ inch

6020100 - 6020115 &	Conc Pavt, Nonreinf, __ inch

6020120 – 6020135	Conc Pavt Reinf, __ inch

6020500 - 6020523	Conc Pavt, High Performance	49-53

6020200 – 6020211	Joint, Contraction, (Type__)

Joint, Expansion, (Type__)

Joint, Plane-of-Weakness, (Type)	54-55

6030035	Non Chloride Accelerator	56

6030040 - 6030053 &	Pavt Repr, Nonreinf Conc, __ inch

6030060 - 6030072	Pavt Repr, Reinf Conc, __ inch	57-60

TABLE OF CONTENTS cont.

PAY ITEM CODE(S)	PAY ITEM DESCRIPTION	PAGE NO.

6030095 - 6030096 &	Sawing and Sealing Pavt Joints

6030100 – 6030101	Resealing Joints with Hot- Poured Rubber	61

7040001	Steel Sheet Piling, Permanent	62

7040002 &	Steel Sheet Piling, Temp

7040003	Steel Sheet Piling, Temp, Left In Place	63

7050020 &	Pile, CIP Conc, Furn and Driven, 12 inch

7050021 &	Test Pile, CIP Conc, 12 inch

7050025	Pile Points, CIP Conc	64-66

7050030 & 7050034	Steel Piles, Furn and Driven, __ inch

7050031 & 7050035	Test Pile, Steel, __ inch

7050039	Pile Point, Steel	67

7060090	Reinforcement, Steel	68

7060092	Reinforcement, Steel, Epoxy Coated	69

7060010 - 7060013 &	Conc, Grade, __

7060100 &	Substructure Conc

7060110 &	Superstructure Conc

7060113	Superstructure Conc, Night Casting	70-72

7060140	Water Repellent Treatment, Penetrating	73

7070050 - 7070071	Structural Steel	74

7070010 - 7070024	Bearing, Elastomeric, __ inch	75

7070040	Shear Developers	76

7080001 - 7080010	Prest Conc Deck, __ inch	77-79

7080015	Post Tensioning (Structure No.)	80

7080021 - 7080041 &	Prest Conc I Beam, __, __ inch

7080051 - 7080096 &	Prest Conc Box Beam, __, __ inch

7080101 - 7080102	Prest Conc 1800 Beam, __	81-82

7100001	Joint Waterproofing	83

7110005	Bridge Railing, Aesthetic Parapet Tube	84-86

7120010 &	Patch, Full Depth

7120015 & 7120016 &	Patching Mortar or Conc

7120110 - 7120115	Patching Concrete, C; C-HE; C-L; C-L-HE; F-L; M	87-89

7120028 – 7120038 &	Adhesive Anchoring of __ Bar, __ inch

7120040 - 7120044	Bolt, Adhesive Anchored, __ inch	90

7120084	Reinforcement, Mechanical Splice	91

7150045	Steel Structure, Cleaning, Type 4	92

7150046	Steel Structure, Coating, Type 4	93

8010001 – 8010004 &	Driveway, Reinf Conc, __ inch

8010005 - 8010008	Driveway, Nonreinf Conc, __ inch	94-97

8020001 – 8020006 &	Curb, Conc, Det __

8020010 &	Curb and Gutter, Bridge Approach

8020015 - 8020040	Curb and Gutter, Conc, Det __	98-101

8030033 - 8030037 &	Sidewalk Ramp

8030043 - 8030047	Sidewalk, Conc, __ inch	102-104

8070000 - 8070008 &	Guardrail, Type __

8070010 - 8070011	Guardrail, Curved, Type __	105-106

8070020 - 8070033	Guardrail Anchorage, Bridge, Detail __	107-108

TABLE OF CONTENTS cont.

PAY ITEM CODE(S)	PAY ITEM DESCRIPTION	PAGE NO.

8070080	Guardrail Reflector	109

8070095	Post, Mailbox	110

8080001	Fence, Woven Wire with Wood Post

8080002	Fence, Woven Wire with Steel Posts	111-113

8100370 - 8100371	Post, Steel, __ Lb	114

8100392 - 8100413	Sign, Type __	115

8110022 - 8110258	Pavement Markings, __	116

8120080 - 8120083	Conc Barrier, Temp, __	117

8120100	Dust Pallative, Applied	118

8120220 - 8120241	Pavt Mrk, Type R and  Pavt Mrk, Type NR	119

8120280 - 8120301	Raised Pavt Mrk, Temp, Type __, (color), (direction)	120

8130005 - 8130012	Riprap, __	121

8160020 - 8160022	Fertilizer, Chemical Nutrient, Cl __	122

8160026	Mulch Anchoring	123

8160027 - 8160028	Mulch Blanket, __	124

8160035 - 8160045	Seeding, Mixture __	125

8160100 - 8160103	Slope Restoration, __	126-127

8160055	Sodding	128

8190330 - 8190346	Luminaire	129

8230150 - 8230181	Water Main	130-131

APPENDIX

DOCUMENT	DOCUMENT DESCRIPTION	PAGE NO.

BOH IM 2007-02	Bridge Construction and

Bridge Deck Construction Inspection	1-7

BOH IM 2011-04	Final Estimate Review Procedure	8-13

BOH IM 2013-01	Special Provision for Source of Steel and Iron

(Buy America) (Supersedes BOH IM 2012-06)	9-20

CA 2007-01	Temporary Concrete Barrier

CA 2011-08	Mandrel Testing of Corrugated Polyethylene Pipe (CPE)\

12SP604(A)	Quality Control and Acceptance of Portland Cement

Concrete (For Local Agency Projects Only)

12SP604(B)	Quality Control and Acceptance of Portland Cement

Concrete

2050001	BACKFILL, SWAMP

Pg 1 of 2 		Pay Unit:  Cubic Yard

MATERIALS:	Granular Material Class III

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Procedures Manual  Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.”
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

- One test per 10,000 cubic yards.

2050001	BACKFILL, SWAMP

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

  - One test per 10,000 cubic yards.

Visual Inspection:	Maximum 500 cubic yards per project

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR .

2.	Measurement and payment

- Engineer will measure volume in original position.

- If it is not practical to calculate the volume in its original position, the engineer will calculate the volume within the limits of the plans, or from soil borings and increase the volume by 15%.

- Density Reports

- Review reports to see that all test and retests meet MDOT requirements 
(see form 0582B) and the minimum frequency of one test per 1000 cubic yards have been achieved.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

NOTE:  Refer to Standard Plan R-103-C

2050010	EMBANKMENT, CIP

Pg 1 of 2 		Pay Unit:  Cubic Yard

MATERIALS:	Granular Material Class II or Granular Material Class III, Sound Earth

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

  - Class II – One test per 3,000 cubic yards.

  - Class III - One test per 10,000 cubic yards.

2050010	EMBANKMENT, CIP

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

        - Class II – One test per 3,000 cubic yards.

        - Class III - One test per 10,000 cubic yards.

Visual Inspection:  Maximum 500 cubic yards per material class per project.

Sound Earth

Visual Inspection:  All material placed.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section.  Tolerance +/- 1 inch if subbase is required and +/- ¾ inch if subbase is not required.

- Measurement and payment.

- Engineer will determine if payment will be based on plan quantity.

b.	Engineer will measure volume based on the grade and cross section shown on the plans if not by plan quantity.

- Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 1000 cubic yards, and regardless of the volume of material placed, a minimum of one test must be taken for each layer.  Sound Earth if used must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

2050011	EMBANKMENT, LM

Pg 1 of 2 		Pay Unit:  Cubic Yard

MATERIALS:	Granular Material Class II or Granular Material Class III, Sound Earth

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

  - Class II – One test per 3,000 cubic yards.

  - Class III - One test per 10,000 cubic yards.

2050011	EMBANKMENT, LM

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards.

- Class III - One test per 10,000 cubic yards.

Visual Inspection:  Maximum 500 cubic yards per material class per project.

Sound Earth

Visual Inspection:  All material placed.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section.  Tolerance +/- 1 inch if subbase is required and +/- ¾ inch if subbase is not required.

- Measurement and payment.

- Engineer will measure by volume, LM.

- Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 1000 cubic yards, and regardless of the volume of material placed, a minimum of one test must be taken for each layer.  Sound Earth if used must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

2050012	EMBANKMENT, STRUCTURE, CIP

Pg 1 of 2	Pay Unit:  Cubic Yard

MATERIALS:	Granular Material Class III, Sound Earth (if allowed)

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

  - Class III - One test per 10,000 cubic yards.

2050012	EMBANKMENT, STRUCTURE, CIP

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

  - Class III - One test per 10,000 cubic yards.

Visual Inspection:  Maximum 500 cubic yards per material class per project.

Sound Earth

- For use under structure footing supported by piling if allowed by Engineer.

Visual Inspection:  All material placed.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment.

- Engineer will measure based on the grade and cross section shown in the plans.

3.	Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 1000 cubic yards, and regardless of the volume of material placed, a minimum of one test must be taken for each layer.

- Original ground must be compacted to 95 percent of maximum unit weight.

- Backfill material must be compacted to 100 percent of maximum unit weight under structure footing for which piling is not specified.

- All density reports are to be placed in ProjectWise on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

2050016	EXCAVATION, EARTH

Pg 1 of 1	Pay Unit:  Cubic Yard

MATERIALS:	Existing Material at Cut Depth

ACCEPTANCE TESTING REQUIREMENTS

Existing Material

- Compact the subgrade to at least 95 percent of its maximum unit weight to a depth of at least 10 inches.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section.  Tolerance +/- 1 inch if subbase is required and +/- ¾ inch if subbase is not required.

- Measurement and payment.

- Engineer will determine if payment will be based on plan quantity.

b.	Engineer will measure volume based on the grade and cross section shown on the plans if not by plan quantity.

- Density Reports.

- Review reports to see that all test and retests meet MDOT requirements 
(see form 0582B) and the minimum frequency of 1 test per 500 feet per width of 24 feet or less.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

2050040	SUBGRADE UNDERCUTTING, TYPE I

Pg 1 of 1	Pay Unit:  Cubic Yard

MATERIALS:	Selected Clay or other Engineer Approved Material

ACCEPTANCE TESTING REQUIREMENTS

Clay

Visual Inspection: All material placed.

Engineer Approved Material

- If approved material is used, follow the acceptance testing requirements from the Current Standard Specification.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section. Tolerance +/- 1 inch if subbase is required and +/- ¾ inch if subbase is not required.

- Measurement and payment.

- Engineer will measure in its original position.

- Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 feet per width of 24 feet or less. Material must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

NOTE:  Refer to Standard Plan R-103-C

2050041	SUBGRADE UNDERCUTTING, TYPE II

Pg 1 of 2 	Pay Unit:  Cubic Yard

MATERIALS:	Granular Material Class II

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files

- Class II - One test per 3,000 cubic yards.

2050041	SUBGRADE UNDERCUTTING, TYPE II

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

  - Class II - One test per 3,000 cubic yards.

Visual Inspection:  Maximum 500 cubic yards per project.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page at the beginning of this document for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section. Tolerance +/- 1 inch if subbase is required and +/- ¾ inch if subbase is not required.

- Measurement and payment.

a.	Engineer will measure in its original position.

- Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 150 feet per width of 24 feet or less. Material must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

NOTE:  Refer to Standard Plan R-103-C

2050042	SUBGRADE UNDERCUTTING, TYPE III

Pg 1 of 1	Pay Unit:  Cubic Yard

MATERIALS:	Excavated Material effectively mixed or Engineer Approved Material

ACCEPTANCE TESTING REQUIREMENTS

Excavated Material

Visual Inspection:  All material placed.

Engineer Approved Material

- If approved material is used in lieu of excavated material, follow the acceptance testing requirements from the Current Standard Specification.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section. Tolerance +/- 1 inch if subbase is required and +/- ¾ inch if subbase is not required.

- Measurement and payment.

a.	Engineer will measure in its original position.

- Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 per width of 24 feet or less. Material must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

NOTE:  Refer to Standard Plan R-103-C

2060002	BACKFILL, STRUCTURE, CIP

Pg 1 of 2	Pay Unit:  Cubic Yard

MATERIALS:	Granular Material Class II

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

  - Class II - One test per 3,000 cubic yards.

2060002	BACKFILL, STRUCTURE, CIP

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

  - Class II - One test per 3,000 cubic yards.

Visual Inspection:  Maximum 500 cubic yards per project.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment.

- Engineer will base payment on plan quantity

- Density Reports.

- Controlled Density Method (subsection 205.03.H.4.a).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 300 cubic yards with 6 inch layers, and regardless of the volume of material placed, a minimum of one test must be taken for each layer.

- Backfill material must be compacted to 95 percent of maximum unit weight.

- Backfill material must be compacted to 100 percent of maximum unit weight in the load bearing area.

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

2080025						EROSION CONTROL, SILT FENCE

Pg 1 of 1 		Pay Unit:  Foot

MATERIALS:	Geosynthetics, Stakes and Lath (Silt Fence)

ACCEPTANCE TESTING REQUIREMENTS

Silt Fence

- A certification from the Approved Manufacturer of the silt fence system.

- Fabric must be on Qualified Product List.

Or

If not from an approved manufacturer then test prior to incorporation. Sample size:  1 sample for the first 3000 ft or fraction thereof; 1 sample for each additional 10,000 ft or fraction thereof; 1 piece 8 ft long by full fence height include 2 attached posts and lath.

Visual Inspection:  Maximum 500 feet.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment.

- Engineer will measure in place excluding overlap.

End of Day ONE

3010002	SUBBASE, CIP

3010003	SUBBASE, LM

Pg 1 of 2 	Pay Unit:  Cubic Yard

MATERIALS: 	Granular Material Class II

ACCEPTANCE TESTING REQUIREMENTS

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files

  - Class II - One test per 3,000 cubic yards.

3010002	SUBBASE, CIP

3010003	SUBBASE, LM

Pg 2 of 2

Job Site/On Site Sources:

- Test reports must be in project files.

  - Class II - One test per 3,000 cubic yards.

Visual Inspection:  Maximum 500 cubic yards per project.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENT

1.	See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Grade checks once every 50 feet across the section. Tolerance + 1 inch.

- Measurement and payment.

a.	Engineer will measure CIP based on cross sections. LM will be based on hauling unit dimensions and load counts.

- Density Reports.

- Refer to section 301 Subbase.  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 feet per width of 24 feet or less. Material must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

3020001	AGGREGATE BASE

3020002	AGGREGATE BASE, LM

3020008 – 3020030	AGGREGATE BASE, __ INCH

Pg 1 of 3 		Pay Unit:	Cubic Yard, Square Yard, Ton

MATERIALS:	Dense Graded Aggregate - 21AA, 21A, 22A

O.G.D.C. by special provision

ACCEPTANCE TESTING REQUIREMENTS

Aggregates

Prequalified Sources:

- One ticket REQUIRED per load containing the following data

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

- If paid by square yard or cubic yard, truck number and time are not required on tickets/documentation.

Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

3020001	AGGREGATE BASE

3020002	AGGREGATE BASE, LM

3020008 – 3020030	AGGREGATE BASE, __ INCH

Pg 2 of 3

- Test reports must be in project files

  - One test per 1,000 tons

Job site/On site Sources:

- Test reports must be in project files

  - One test per 1,000 Tons

  - Weigh Tickets required if paid by ton

Visual Inspection:  Maximum VI 500 tons per material class per project

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Immediate possession of tickets is required if paying by ton (weight).

- Moisture check required on ton pay items by inspector and note on the IDR.

- Depth checks required.  One test per 400 lft per traffic lane width.  One test per 1,200 syds for intersections, crossovers, ramps, widening strips, and acceleration lanes.  Note depth checks on IDR for SYD pay item specified depth.

- Grade checks required once every 50 feet across the section.
Tolerance +/- 1/2 inch.

- Measurement and payment

  - Tons: Engineer will measure scale weight of the material, including ad mixtures and moisture content no greater than 6%, if over 6% refer to section 109.01.

  - LM: Engineer will measure based on hauling unit dimensions and load count before placement and compaction.

  - SYD: Engineer will measure based on the width and length for the specified depth as shown on the plans.

3020001	AGGREGATE BASE

3020002	AGGREGATE BASE, LM

3020008 – 3020030	AGGREGATE BASE, __ INCH

Pg 3 of 3

- Density Reports

- Refer to subsection 302.03A, Placing and Compacting.  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 feet per width of 24 feet or less.

- Backfill material must be compacted to 95 percent of maximum unit weight under concrete

- Backfill material must be compacted to 98 percent of maximum unit weight under HMA pavement.

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

3030004 – 3030006	OPEN-GRADED DR CSE, __ INCH

Pg 1 of 2	Pay Unit:	Square Yard

MATERIALS:	Open Graded Aggregate 4G, See special provisions in the proposal

ACCEPTANCE TESTING REQUIREMENTS

Aggregates

Prequalified Sources:

- One ticket REQUIRED per load containing the following data

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files

- One test per 1,000 Tons

3030004 – 3030006	OPEN-GRADED DR CSE, __ INCH

Pg 2 of 2

Job site/On site Sources:

- Test reports must be in project files

- One test per 1,000 Tons

Visual Inspection:  Maximum 100 Ton per material class

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Depth checks required.  One test per 400 lft per traffic lane width.  One test per 1,200 syds for intersections, crossovers, ramps, widening strips, and acceleration lanes.  Note depth checks on IDR.

- Measurement and payment

- Engineer will measure and the department will pay for OGDC according to the contract.

- Density Reports

- Refer to contract documents. Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency requirement per the contract.

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

3050002	HMA BASE CRUSHING AND SHAPING

Page 1 of 1	Pay unit:	Square Yard

MATERIALS:	If required 21A, 21AA, 22A, (to be paid separately as aggregate base)

ACCEPTANCE TESTING REQUIREMENTS

Job site/On site Sources:

Visual Inspection:   All material placed.  Check specification for gradation requirements on

crushed material.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENT

1.	See Notes page for IAT requirements.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- After final Shaping, grade checks once every 50 feet across the section. Tolerance +/- 1/2 inch when tested with a 10 foot straightedge.

- Measurement and payment

a.	Engineer will measure based on plan quantity in accordance with standard specifications 109.01A regardless of any variations in depth.

- Density Reports

- Refer to subsection 305.03C, Compacting and Shaping in the standard specifications. Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 feet per width of 24 feet or less. Material must be compacted to 98 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

3060005 – 3060006	AGGREGATE SURFACE CSE

3060010 – 3060016	AGGREGATE SURFACE CSE, __ INCH

Pg 1 of 2 		Pay Units:	Ton, Cubic Yard, Square Yard

MATERIALS:	Dense Graded Aggregate 21A, 21AA, 22A, or 23A

ACCEPTANCE TESTING REQUIREMENTS

Aggregates

Prequalified Sources:

- One ticket REQUIRED per load containing the following data

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

- If paid by square yard or cubic yard, truck number and time are not required on tickets/documentation.

- Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files

  - One test per 1,000 Tons.

3060005 – 3060006	AGGREGATE SURFACE CSE

3060010 – 3060016	AGGREGATE SURFACE CSE, __ INCH

Page 2 of 2

Job site/On site Sources:

- Test reports must be in project files

- One test per 1,000 Tons

Visual Inspection:  Maximum VI is 500 Tons per material class per project

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS (IAT)

1.	See Notes page for IAT requirements

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Immediate possession of tickets is required if paying by ton (weight).

- Moisture check required on ton pay items by inspector and note on the IDR.

- Depth check required.  One test per 400 lft per traffic lane width.  One test per 1,200 syds for intersections, crossovers, ramps, widening strips, and acceleration lanes.  Note depth checks on IDR for SYD pay item specified depth.

- Grade checks required once every 50 feet across the section. Tolerance +/- 1/2 inch.

- Measurement and payment

  - Tons: Engineer will measure scale weight of the material, including ad mixtures and moisture content no greater than 6%, if over 6% refer to section 109.01.

  - SYD: Engineer will measure based on the width and length for the specified depth as shown on the plans.

  - CYD: Engineer will measure based on hauling unit/load count for LM or computations for CIP.

- Density Reports

- Controlled Density Method (subsection 306.03b).  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 feet per width of 24 feet or less. Material must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

3070001 – 3070051	APPROACH, CL I; CL II AND CL III

3070101 – 3070162	SHOULDER, CL I; CL II; CL III AND CL IV

Pg 1 of 2 		Pay Units:  Ton, Cubic Yard, Square Yard

MATERIALS:	Dense Graded Aggregate 21A, 21AA, 22A, 23A or Salvaged Material

ACCEPTANCE TESTING REQUIREMENTS

Aggregates

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ___________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

  - One test per 1,000 Tons

3070001 – 3070051	APPROACH, CL I; CL II AND CL III

3070101 – 3070162	SHOULDER, CL I; CL II; CL III AND CL IV

Pg 2 of 2

Job site/On site Sources:

- Test reports must be in project files.

- One test per 1,000 Tons

Visual Inspection:  Maximum 500 Tons per material class per project.

Salvaged Material

Visual Inspection:  All material for 2 inch maximum particle size, document on IDR.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Immediate possession of tickets is required if paying by ton (weight).

- Moisture check required on ton pay items by inspector and note on the IDR.

- Depth check required: One test per 400 lft per traffic lane width. One test per 1,200 syds for intersections, crossovers, ramps, widening strips, and acceleration lanes.
Note depth checks on IDR for SYD items.

- Measurement and payment.

  - Tons: Engineer will measure scale weight of the material, including ad mixtures and moisture content no greater than 6%, if over 6% refer to section 109.01.

  - LM: Engineer will measure based on hauling unit dimensions and load count before placement and compaction.

  - SYD: Engineer will measure based on the width and length for the specified depth as shown on the plans.

- Density Reports.

- Refer to subsection 307.03C, Placing and Compacting.  Review reports to see that all test and retests meet MDOT requirements (see form 0582B) and the minimum frequency of one test per 500 feet per width of 24 feet or less.

- Class I must be compacted to 98 percent of maximum unit weight, Class II, Class III and Class IV must be compacted to 95 percent of maximum unit weight.

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

3080005	Geotextile, Separator

3080010	Geotextile, Stabilization

Page 1 of 1	Pay unit:	Square Yard

MATERIALS:	Separator Geotextile and Stabilization Geotextile.

ACCEPTANCE TESTING REQUIREMENTS

Test for Acceptance allow up to 28 days.

Job site/On site Sources:

Visual Inspection:   Maximum 500 syd per material type per project.

CONSTRUCTION

1.  Inspector’s Daily Report

  - IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

  - All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

a.	The Engineer will measure Geotextile, Separator and Geotextile, Stabilization in place, to the limits shown on the plans.

4010012 – 4010108	CULVERT END SECTIONS

Pg 1 of 1 		Pay Unit:  Each

MATERIALS:	Concrete End Section, Metal End Section

ACCEPTANCE TESTING REQUIREMENTS

End Section

- Concrete End Section.

  - Certification from Approved Manufacturer.

Or

  - Test per lot prior to incorporation.  Test 1 percent of pieces per the Materials Quality Assurance Manual.

Visual Inspection: Maximum 10 pieces

- Metal End Section.

  - General Certification.

Visual Inspection: Maximum 4 pieces

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note The unit price for Culv End Sect, Metal also includes the cost of providing and placing the length of associated culvert represented by the "c" dimension shown on the plans, per section 401.04 of the Current Standard Specification.

- Measurement and payment.

- Engineer will base payment for each end section used.

4010131 – 4010698	CULVERTS

Pg 1 of 3	Pay Unit:  Foot

MATERIALS: 	Aggregate 6A,17A, 34R, Granular Material Class II, III, IIIA, Geosynthetic, Joint Sealers, Pipe Gaskets, Reinforced/Nonreinforced Concrete pipe, or Corrugated & Spiral Ribbed Al-Alloy/Steel pipe, Smooth-Lined Corrugated Plastic Pipe(CPE, HDPE and CPV), Water Tight Joint

ACCEPTANCE TESTING REQUIREMENTS

Aggregates & Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

- Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

4010131 – 4010698	CULVERTS

Pg 2 of 3

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards

- Class III – One test per 10,000 cubic yards

- Class IIIA – One test per 1,000 cubic yards

- Aggregates 6A,17A and 34R  – One test per 1,000 tons

Job site/On site Sources:

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards

- Class III – One test per 10,000 cubic yards

- Class IIIA – One test per 1,000 cubic yards

Visual Inspection:

Class II – Maximum 500 cubic yards per project..

Class III – Maximum 500 cubic yards per project.

Class IIIA – Maximum 100 cubic yards per project.

Aggregates 6A,17A and 34R – Maximum 100 tons per material class per project.

Geosynthetics

- Geotextile blanket – Test for acceptance

Visual Inspection:  Maximum 500 Syd

Joint Sealers

- Cold applied joint sealers (Mastic).

a.	VI

Pipe

- Concrete and Steel Pipe.

  - A Certification from the Approved Manufacturer.

Or

  - Test prior to incorporation.  Test per the Materials Quality Assurance Procedures Manual.

Visual Inspection:  Maximum 10 pieces Conc. Non Reinforced, 5 pieces 42 inch or less Conc Reinforced, 125 ft steel 12 inch or less, 50 ft steel 15 inch to 54 inch, 25 ft 60 inches or greater.

- Plastic Pipe.

- Shipment of Tested Stock Report, Form 1922, from approved source.

Note: Class A, B and F plastic pipe must be from QPL (909.06).

Or

4010131 – 4010698	CULVERTS

Pg 3 of 3

- Test prior to incorporation.  One per 1,000 feet for 12 inch diameter and over.

Note: All Class A, B and F plastic pipe must be from QPL (909.06).

Visual Inspection:  Maximum 100 ft 12 inch and greater.

- Aluminum Alloy Pipe.

- A General Certification

Visual Inspection:  Maximum 250 ft

NOTE:  Mandrel testing required only for all plastic pipe 12 Inches to 48 Inches. For additional information Refer to
CA-2011-08, or as superseded, for additional information.  Video inspection required per subsections 401.03.C.1 and 401.03.M.

Water Tight Joint System

- Water Tight Joint/Gaskets.

  - Must be on Qualified Product List.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENT ASSURANCE TEST (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Check for the 12SP401B or Current SP for wrapping all Joints

Note: Refer to Standard Plan R82

- Measurement and payment.

- Engineer will measure culverts of the diameter, class or material required, by length, excluding the length of the end sections as shown on the plans.

- Density Reports.

- Review reports to see that all test and retests meet MDOT requirements 
(see form 0582B).

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

4020001 – 4021133	SEWER, CL __, __ INCH, TR DET __

Pg 1 of 4	Pay Unit:  Foot

MATERIALS: 	Aggregate 6A,17A, 34R , Granular Materials Class II, III, IIIA, Geosynthetics, Joint Sealers, Reinforced/Non-reinforced Concrete Pipe, or Corrugated & Spiral Ribbed Al-Alloy/Steel Pipe, Smooth-Lined Corrugated Plastic Pipe(CPE and HDPE), Corrugated Polyvinyl Chloride Pipe(CPV, CPVC and PVC), Steel Pipe Jacked-in-Place, Water Tight Joint System

ACCEPTANCE TESTING REQUIREMENTS

Aggregate/Granualar Material

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

- Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

4020001 – 4021133	SEWER, CL __, __ INCH, TR DET __

Pg 2 of 4

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards

- Class III – One test per 10,000 cubic yards

- Class IIIA – One test per 1,000 cubic yards

- Aggregates 6A,17A and 34R – One test per 1000 tons

Job site/On site Sources

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards

- Class III – One test per 10,000 cubic yards

- Class IIIA – One test per 1,000 cubic yards

Visual Inspection

Class II – Maximum 500 cubic yards per project

Class III – Maximum 500 cubic yards per project

Class IIIA – Maximum 100 cubic yards per project

Aggregates 6A,17A and 34R  – Maximum 100 tons per material class per project

Geosynthetic

- Geotextile Blanket – Test for Acceptance

Visual Inspection:  Maximum 500 Syd

Joint Sealers:

- Cold applied joint sealers (Mastic).

  - VI.

Pipe

- Corrugated Polyvinyl Chloride Pipe (CPV, CPVC and PVC).

- Test prior to incorporation.  One test per 1000 feet of 12 inch or greater diameter straight lengths of pipe.

- Corrugated Polyethylene pipe (CPE and HDPE)

  - Shipment of Tested Stock Report, Form 1922, from approved source.

Or

  - Test prior to incorporation.  One per 1,000 feet for 12 inch diameter and over.

NOTE:  All Class A, B and F Plastic Pipe CPE. HDPE, CPV, CPVC and PVC must be on Qualified Product List

Visual Inspection:  Maximum 100 ft. 12 inches or greater.

- Concrete/Steel Pipe.

- A Certification from the Approved Manufacturer.

Or

- Test prior to incorporation.  Test 1 percent of number of pieces of each size.  Test per the Materials Quality Assurance Procedures Manual.

4020001 – 4021133	SEWER, CL __, __ INCH, TR DET __

Pg 3 of 4

Visual Inspection:  Maximum 10 pieces Conc. Non Reinforced, 5 pieces 42 inch or less Conc Reinforced., 125 ft steel 12 inch or less, 50 ft steel 15 inch to 54 inch, 25 ft 60 inches or greater.

- Aluminum Alloy Pipe

  - A General Certification

AND

  - Test prior to incorporation.  One test per 1000 feet of pipe.

Visual Inspection:  Maximum 250 ft

- Steel Pipe, Jacked-in-Place

- A General Certification

Water Tight Joint/Gaskets

- VI and must be on Qualified Product List for Compression or External 	Rubber Type.  VI as part of the Watertight Joint System and note on IDR.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENCE ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

4020001 – 4021133	SEWER, CL __, __ INCH, TR DET __

Pg 4 of 4

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Check for the 12SP401B or Current SP for wrapping all Joints

Note: Refer to Standard Plan R-83

- Measurement and payment.

  - Engineer will measure Sewer and Sewer, Reinf conc, Ellip of the size, class, and trench detail required, in-place from center to center of manhole, catch basin, or inlet.

  - Engineer will measure Sewer, Jack in Place, of the size and class required, by multiplying the number of units jacked by the commercial laying length.

- Density Reports.

- Review reports to see that all test and retests meet MDOT requirements (see form 0582B).

- All density reports are to be placed in ProjectWise on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

4030010 – 4030090	DR STRUCTURE COVER , Type _ XX

Pg 1 of 1	Pay Units:  Ea

MATERIALS:	Castings, malleable iron and steel

ACCEPTANCE TESTING REQUIREMENTS

Malleable iron and steel

Visual Inspection:  All material placed

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Refer to Standard Plans R-7, R-8, R-8X, R-9, R-9X, R-10, R-12, R-14, R-15, R-18, R-20, R-20D, R22, R-23, and R-24.

- Measurement and payment

- Engineer will measure drainage structure covers based on placed quantity.

4030200 – 4030271	DR STRUCTURE, __ INCH DIA

Pg 1 of 5	DR STRUCTURE, ADD DEPTH, __ INCH DIA, 8 TO 15	FT

DR STRUCTURE, ADD DEPTH, __ INCH DIA, OVER 15 FT

Pay Unit:  Each, Ft

MATERIALS:	Mortar Standard, Granular Material Class II, III, Steel Reinforcement, Concrete Brick or Block, Pre-cast Reinforced Concrete Units, Manhole Bases & Sumps, Concrete Grade S3

ACCEPTANCE TESTING REQUIREMENTS

Mortar

- Standard, VI and document on IDR

GRANULAR MATERIALS

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

- Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable.

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

4030200 – 4030271	DR STRUCTURE, __ INCH DIA

Pg 2 of 5	DR STRUCTURE, ADD DEPTH, __ INCH DIA, 8 TO 15	FT

DR STRUCTURE, ADD DEPTH, __ INCH DIA, OVER 15 FT

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards

- Class III – One test per 10,000 cubic yards

Job site/On site Sources:

- Test reports must be in project files.

- Class II – One test per 3,000 cubic yards

- Class III – One test per 10,000 cubic yards

Visual Inspection:

Class II – Maximum 500 cubic yards per project

Class III – Maximum 500 cubic yards per project

Concrete Brick and Block

- A Test Data Certification.

Visual Inspection:  Maximum 1,000 pieces each.

Pre-cast Reinforced Concrete Units

- A General Certification from the Approved Manufacturer.

Or

- Test prior to incorporation.  Test 1 percent per each size.  Test per the Materials Quality Assurance Procedures Manual.

Visual Inspection:  Maximum 10 pieces.

Pre-cast Concrete Bases

- A General Certification from the Approved Manufacturer

Or

- Test prior to incorporation.  Test 5 percent of total

Visual Inspection:  Maximum 10 pieces

4030200 – 4030271	DR STRUCTURE, __ INCH DIA

Pg 3 of 5	DR STRUCTURE, ADD DEPTH, __ INCH DIA, 8 TO 15	FT

DR STRUCTURE, ADD DEPTH, __ INCH DIA, OVER 15 FT

Concrete Grade S3

Note: Refer to 12SP604 for concrete QC/QA requirement

NRMCA Plants

- Plant

a.	Current NRMCA certification

- Scales Check

- Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

- Copy in project files

For Portable Batch Plants

1.	Plant

  - Documentation of Inspection after each move per 601.03.A.1.a.

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

- Scales Check

  - Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Copy in project files

For all Plants

- Cement

  - A General Certification from the Approved Manufacturer.

Visual Inspection:  Maximum VI 45 tons

4030200 – 4030271	DR STRUCTURE, __ INCH DIA

Pg 4 of 5	DR STRUCTURE, ADD DEPTH, __ INCH DIA, 8 TO 15	FT

DR STRUCTURE, ADD DEPTH, __ INCH DIA, OVER 15 FT

- Coarse Aggregates

  - Test prior to incorporation.  One test per 1,000 tons.  Maximum VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

Visual Inspection:  Maximum 100 tons for total grade used on job

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

Visual Inspection:  Maximum 100 tons for total FA used on job

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

c.	GGBFS: Approved Manufacturer

- Concrete Admixtures

- VI and must be on Qualified Product List .

- Fly Ash

- A General Certification from the Approved Manufacturer

- GGBFS

a.	A General Certification from the Approved Manufacturer.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

4030200 – 4030271	DR STRUCTURE, __ INCH DIA

Pg 5 of 5	DR STRUCTURE, ADD DEPTH, __ INCH DIA, 8 TO 15	FT

DR STRUCTURE, ADD DEPTH, __ INCH DIA, OVER 15 FT

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Refer to Standard Plans R-1, R-2, R-3, and R-4

- Measurement and payment

- Engineer will base payment for DR STRUCTURE, INCH DIA. from 0 to 8 feet as each.

- Additional payment is required for

  - DR STRUCTURE, ADD DEPTH, __ INCH DIA, 8 FT TO 15  FT will be paid by the foot

  - DR STRUCTURE, ADD DEPTH, __ INCH DIA, OVER 15 FT will be paid by the foot.

- Density Reports

- Review reports to see that all test and retests meet MDOT requirements (see form 0582B).

- All density reports are to be placed in ProjectWise on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual.

- Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

End of Day Two and 6

4040001 – 4040089	UNDERDRAIN (Subgrade, Bank, Fdn., Subbase,

Pipe, PDS and Edge of Pavt.)

4040091 – 4040099	UNDERDRAIN OUTLETS

Pg 1 of 3		Pay Unit:  Foot

MATERIALS:	OGDC Aggregate (34R), Granular Material Class IIAA, Geosynthetics, Prefabricated Drainage System (PDS), Corrugated Plastic Tubing, Acrylonitrile-Butadiene-Styrene Pipe (ABS), Smooth Plastic Pipe and Corrugated Steel Pipe.

ACCEPTANCE TESTING REQUIREMENTS

Aggregate/Granular Materials

Prequalified Sources:

- One ticket per load containing

- MDOT aggregate source number

- Date and time of shipment

- MDOT Control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.

Date _______________       Signature ______________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket per load containing

- MDOT aggregate source number

- Date and time of shipment

- MDOT Control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

h.	If paid by square yard or cubic yard, truck number and time are not required on tickets/documentation

4040001 – 4040089	UNDERDRAIN (Subgrade, Bank, Fdn., Subbase,

Pipe, PDS and Edge of Pavt.)

4040091 – 4040099	UNDERDRAIN OUTLETS

Pg 2 of 3

- Test reports must be in project files

- Class IIAA – See the Aggregate Manual for Testing Frequency

- Aggregates 34R  – One test per 1,000 tons

Job site/On site Sources:

- Test reports must be in project files

- Class IIAA – See the Aggregate Manual for Testing Frequency

Visual Inspection:

Class IIAA – See the Aggregate Manual for Maximum VI

34R – Maximum 100 Tons

Geosynthetics

- Geotextile Blanket

  - Test prior to incorporation

Visual Inspection:  Maximum 500 Syd.

Underdrain

- Corrugated Steel Pipe

  - A General Certification from the Approved Manufacturer.

Or

  - Test prior to incorporation.  Test per Section 4.02 of the Materials Quality Assurance Procedures Manual.

Visual Inspection:  Maximum 125 feet 12 inch or less, 50 ft, 15 inch to 54 inch

- Smooth Plastic Pipe

- Test prior to incorporation.  One test per 2,500 feet or fraction thereof

Visual Inspection:  Maximum 250 feet

- Corrugated Plastic Tubing (PE or PVC) (wrapped and unwrapped)

a.	A General Certification from approved manufacturer.

Or

- Test prior to incorporation.  One test per 5,000 feet with sample from coil.

Visual Inspection:  Maximum 250 feet.

4040001 – 4040089	UNDERDRAIN (Subgrade, Bank, Fdn., Subbase,

Pipe, PDS and Edge of Pavt.)

4040091 – 4040099	UNDERDRAIN OUTLETS

Pg 3 of 3

- Prefabricated Drainage System (910.05)

  - A Test Data Certification from approved manufacturer

Or

  - Test prior to incorporation. One test per 10,000 feet or less.

- Acrylonitrile-Butadiene-Styrene Pipe (ABS, Misc # 7)

  - Test prior to incorporation. One test per 6,000 feet or less.

Visual Inspection:  Maximum 600 feet

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Refer to Standard Plans R-80

- Measurement and payment

  - Engineer will measure underdrains in place.

- Density Reports

- Review reports to see that all test and retests meet MDOT requirements 
(see form 0582B).

- All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

4040111 – 4040115	UNDERDRAIN, OUTLET ENDING, __INCH

Pg 1 of 1	Pay Unit:  Each

MATERIALS:	Concrete or Steel End Section with Rodent Screen

ACCEPTANCE TESTING REQUIREMENTS

Outlet Ending

1.	Steel

Visual Inspection: All material placed of complete unit and note on IDR.

2.	Concrete

Visual Inspection: All material placed and note on IDR.

3.	Rodent Screen

Visual Inspection: All material placed and note on IDR.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Refer to Standard Plans R-80

- Measurement and payment

- Engineer will measure each outlet ending in place.

5010025 – 5010806	HMA, __; HMA Approach

Pg 1 of 2	Pay Unit:  Ton, Square Yard

MATERIALS:	Asphalt Binder, Emulsified Asphalt (Bond Coat), and HMA Mixture

Note: Refer to SP 501 U and SP 501 V SUPERPAVE HOT MIX ASPHALT PERCENT WITHIN LIMITS (PWL)

ACCEPTANCE TESTING REQUIREMENTS

Asphalt Binder

- A General Certification from the Approved Certifier.

Or

- Test prior to incorporation.  One test per day per contractor’s tank of asphalt binder.

NOTE:

Daily Asphalt Binder Sample: Contractor shall submit one sample per grade, per project, per day of production for certification verification (see form 1923B).

Witness Sample: The Engineer may request to witness the sampling of the asphalt binder upon any visit to the HMA plant.  The engineer will complete the 1923B form for the witness sample.  The witness sample will become the daily asphalt binder sample of record.  Any other binder sample taken that same day will be discarded.

Failing binder notification letters must be in the project files.

Emulsified Asphalt (Bond Coat)

- A General Certification from approved manufacturer.

Or

- Test prior to incorporation.

HMA Mixtures

HMA Plant:

- Plant certification will be verified by RMI on Form 1911. JMF (Job Mix Formula) Form 1911 must be in project file.

5010025 – 5010806	HMA, __; HMA Approach

Pg 2 of 2

HMA mixture

- Test for acceptance. A written statement from the supplier certifying all materials used in mix are of the same source submitted for JMF. This requirement must be met by separate letter in file from producer.

Visual Inspection:  Maximum 500 tons per project per mix.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

2.	HMA Mixtures testing in the lab.

- Contact Region IAT Coordinator or Region Mix Inspector (RMI) to schedule IAT as soon as possible.  One satisfactory test/per sampler and tester/per season.  A certified bituminous technician is required for testing on all state and federally funded projects.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay. Including Temperature and Yield calculations

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Delivery tickets required per load which includes control section/job number, mix type, date, time, truck number, tare weight, tonnage delivered and accumulated tonnage.

- Immediate possession of tickets is required if paying by ton (weight).

- HMA sampling needs to be obtained by a qualified technician, to be qualified contact the RMI.

- Measurement and payment

- Engineer will measure and pay for HMA of the mix specified based on weight placed as supported by weigh tickets.

- Additional Documentation Requirements in project file

- Form 1903B Verification/Acceptance Report (minimum frequency, one report per lot placed)

- Form 1903C Report of Contractor’s Quality Control Tests

- Form 1907 Core Density

- Form 1907J Joint Core Density

- MDOT QA Plan

- Contractor QC Plan

- Random number sheets signed by MDOT and Contractor

- Pre-production meeting minutes

- PWL Calculation spreadsheet (if required)

- Local Agency Projects

- Form 1903 Daily report of bit plant inspection for each day of production. Check special provision for additional requirements.

- Density Reports

- Refer to section 501 HMA Construction Practices.  One test per 1000 feet, width of 24 feet (minimum) or as defined per special provision if any in the proposal.

- All density reports are to be placed in ProjectWise on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum.

6020002 – 6020010	CONC BASE CSE, REINF, __ INCH

6020015 – 6020023	CONC BASE CSE, NONREINF, __ INCH

6020030 – 6020031	CONC, GRADE __

6020050 – 6020062	CONC PAVT, MISC, NONREINF, __ INCH

6020070 – 6020082	CONC PAVT, MISC, REINF, __ INCH

6020100 – 6020115	CONC PAVT, NONREINF, __ INCH

6020120 – 6020135	CONC PAVT, REINF, __ INCH

6020500 – 6020523	CONC PAVT, HIGH PERFORMANCE

Pg 1 of 5 	Pay Unit:  Square Yard, Cubic Yard

MATERIALS:	Adhesive System, Bituminized Fiber Joint Filler, Concrete Grade P1, P1-M and P2, Curing Compound-White, Hot Poured Rubber, Lane Tie bars, Wire Fabric

Note: Refer to 12SP604 for concrete QC/QA requirement

ACCEPTANCE TESTING REQUIREMENTS

Adhesive System

- VI and must be on Qualified Product List

- Pull out test required per section 602.03.F.2 on form 1928

Bituminized Fiber Joint Filler

- A Test Data Certification.

Visual Inspection:  Maximum 150 square feet for all other sizes.

Concrete Grade P1, P1-M, P2

NRMCA Plants

1.	Plant

a.	Current NRMCA certification.

2.	Scales Check

a.	Inspection certification every 6 months.

3.	Dispenser Check

a.	Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For Portable Batch Plants

1.	Plant

  - Documentation of Inspection after each move per 601.03.A.1.b.  With Waiver certification per 601.03.C from the Engineer

6020002 – 6020010	CONC BASE CSE, REINF, __ INCH

6020015 – 6020023	CONC BASE CSE, NONREINF, __ INCH

6020030 – 6020031	CONC, GRADE __

6020050 – 6020062	CONC PAVT, MISC, NONREINF, __ INCH

6020070 – 6020082	CONC PAVT, MISC, REINF, __ INCH

6020100 – 6020115	CONC PAVT, NONREINF, __ INCH

6020120 – 6020135	CONC PAVT, REINF, __ INCH

6020500 – 6020523	CONC PAVT, HIGH PERFORMANCE

Pg 2 of 5

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

- Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

Materials

1.	Cement

  - General Certification from the Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse/Intermediate Aggregates

  - Test prior to incorporation.  One test per 1,000 tons.  Maximum VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

  - See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons for total grade used on job

- Fine Aggregate

  - Test prior to incorporation.  One test per 1,000 tons.

  - See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons for total FA used on job

6020002 – 6020010	CONC BASE CSE, REINF, __ INCH

6020015 – 6020023	CONC BASE CSE, NONREINF, __ INCH

6020030 – 6020031	CONC, GRADE __

6020050 – 6020062	CONC PAVT, MISC, NONREINF, __ INCH

6020070 – 6020082	CONC PAVT, MISC, REINF, __ INCH

6020100 – 6020115	CONC PAVT, NONREINF, __ INCH

6020120 – 6020135	CONC PAVT, REINF, __ INCH

6020500 – 6020523	CONC PAVT, HIGH PERFORMANCE

Pg 3 of 5

- Liquid Concrete Admixtures

- a.	VI and must be on Qualified Product List (903.01, 903.02 & 903.03).

- GGBFS

  - General Certification from the Approved Manufacturer

- Fly Ash

- General Certification from the Approved Manufacturer

Curing Compound

- A Test Data Certification.

NOTE: Must be used within one year of manufacturer date.

Visual Inspection:  Maximum 200 gallons for total material used on project.

Hot Poured rubber

- Per Special Provision 12SP914B

Lane Tie Bars

- A General Certification from the Approved Manufacturer for Bar

- Coating Company is an Approved Manufacturer

- Coating is a VI and must be on Qualified Product List (905.03C1).

Or

Test prior to incorporation.  One test per project per manufacturer.

Visual Inspection:  Maximum 500 pounds

NOTE:  Pullout test required – Documentation placed in the Project Files.

6020002 – 6020010	CONC BASE CSE, REINF, __ INCH

6020015 – 6020023	CONC BASE CSE, NONREINF, __ INCH

6020030 – 6020031	CONC, GRADE __

6020050 – 6020062	CONC PAVT, MISC, NONREINF, __ INCH

6020070 – 6020082	CONC PAVT, MISC, REINF, __ INCH

6020100 – 6020115	CONC PAVT, NONREINF, __ INCH

6020120 – 6020135	CONC PAVT, REINF, __ INCH

6020500 – 6020523	CONC PAVT, HIGH PERFORMANCE

Pg 4 of 5

Welded Wire Fabric

- General Certification from the Approved Manufacturer

Or

- Test prior to incorporation.  One test per project per manufacturer.

Visual Inspection:  Maximum 500 square yards.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.   Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174R - Inspector’s Report of Concrete Placed - roadway.  One report per day of placement completely filled out. Document all underruns.

- Contractors QC documentation

Note: Refer to Standard Plan R-41

- Measurement and payment

  - Engineer will measure and determine quantity.

6020002 – 6020010	CONC BASE CSE, REINF, __ INCH

6020015 – 6020023	CONC BASE CSE, NONREINF, __ INCH

6020030 – 6020031	CONC, GRADE __

6020050 – 6020062	CONC PAVT, MISC, NONREINF, __ INCH

6020070 – 6020082	CONC PAVT, MISC, REINF, __ INCH

6020100 – 6020115	CONC PAVT, NONREINF, __ INCH

6020120 – 6020135	CONC PAVT, REINF, __ INCH

6020500 – 6020523	CONC PAVT, HIGH PERFORMANCE

Pg 5 of 5

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

6020200 - 6020211	JOINT, CONTRACTION, (TYPE____)

Pg 1 of 2	JOINT, EXPANSION, (TYPE____)

JOINT, PLANE –OF- WEAKNESS, (TYPE____)

Pay Unit:  Foot

MATERIALS:	Backer Rod, Expansion Caps, Hot Poured Rubber Sealant, Joint Filler Fiber, Load Transfer Assemblies

ACCEPTANCE TESTING REQUIREMENTS

Backer Rod

- VI and document on IDR

Dowel Bars

- A General Certification from the Approved Manufacturer for Bar

- Coating Company is an Approved Manufacturer

- Coating is a VI and must be on Qualified Product List (905.03C1).

Or

Test prior to incorporation.  One test per project per manufacturer.

Visual Inspection:  Maximum 1200 Bars

Expansion Caps

Visual Inspection: All material placed must conform to Standard Plan R-40 series, and Buy America

Hot Poured Joint Sealant

- Per Special Provision 12SP914B

Joint Filler Fiber

- Test Data Certification

Visual Inspection:  Maximum VI 150 square feet for all other sizes.

Recycled Rubber Joint Filler

    - VI and must be on Qualified Product List

6020200 - 6020211	JOINT, CONTRACTION, (TYPE____)

Pg 2 of 2	JOINT, EXPANSION, (TYPE____)

JOINT, PLANE –OF- WEAKNESS, (TYPE____)

Load Transfer Assemblies

- General Certification from an Approved manufacturer for Assemblies

- General Certification from an Approved manufacturer for the Bars

- General Certification from an Approved manufacturer for the Coating company

- VI and must be on Qualified Product List of the Coating.

- VI and must be on Qualified Product List of the Bond release agent

- Fabrication inspection of the Assemblies, minimum one inspection per manufacturer per project, on Form 0553.

Visual Inspection:  Maximum 100 assemblies

NOTE:

Each Bundle of Assemblies need to have a tag on them with the assembly manufacturer name and plant location, Control section/project number, Lot number or other identification that will also be shown on the accompanying certification, and Supplier and/or contractor’s name.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- Inspection of the Load Transfer Assemblies needs to be completed on form 0553, and placed in the Project Files.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Refer to Standard Plans R-37, R-39, R-40, R-42, R-43

- Measurement and payment

- Engineer will pay based on measurement

6030035	NON CHLORIDE ACCELERATOR

Pg 1 of 1	Pay Unit:  Gal

MATERIALS:	Non-Chloride accelerator

ACCEPTANCE TESTING REQUIREMENTS

Non Chloride Accelerator

- VI and must be on Qualified Product List (903.04)

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure and pay based on the quantity printed on the automated batch ticket.

6030040 – 6030053	PAVT REPAIR, NONREINF CONC, __ INCH

6030060 – 6030072	PAVT REPR, REINF CONC, __ INCH

Pg 1 of 4	Pay Unit:  Square Yard

MATERIALS:	Adhesive System, Concrete Grade P1, P1-M, P-MS and P-NC, Curing Compound-White, Hot Poured Rubber, Insulation Blankets, Lane Tie Bars Wire Fabric

ACCEPTANCE TESTING REQUIREMENTS

Adhesive system

- VI and must be on Qualified Product List(712.03J).

Concrete Grade P1, P1-M, P-MS and P-NC

NRMCA Plants

1.	Plant

a.	Current NRMCA certification.

2.	Scales Check

a.	Inspection certification every 6 months.

3.	Dispenser Check

a.	Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

a.	Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

Materials

1.	Cement

- General Certification from the Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

6030040 – 6030053	PAVT REPAIR, NONREINF CONC, __ INCH

6030060 – 6030072	PAVT REPR, REINF CONC, __ INCH

Pg 2 of 4

- Coarse Aggregates

  - Test prior to incorporation.  One test per 1,000 tons L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

Visual Inspection:  Maximum 100 tons for total grade used on job

  - See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

Visual Inspection:  Maximum 100 tons for total FA used on job.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- GGBFS

- General Certification from the Approved Manufacturer

- Fly Ash

- General Certification from the Approved Manufacturer

- Liquid Concrete Admixtures

a.	VI and must be on Qualified Product List (903.01, 903.02 & 903.03).

Curing Compound

- A Test Data Certification.

NOTE:  Must be used within one year of manufacturer date.

Visual Inspection:  Maximum 200 gallons.

6030040 – 6030053	PAVT REPAIR, NONREINF CONC, __ INCH

6030060 – 6030072	PAVT REPR, REINF CONC, __ INCH

Pg 3 of 4

Hot Poured Joint Sealant

- Per Special Provision 12SP914B

Insulation Blankets

- A Test Data Certification

Visual Inspection:  Maximum 10 sheets.

Lane Tie Bars

- A General Certification from the Approved Manufacturer for Bar

- A General Certification from the Approved Manufacturer for the Coating Company

- VI and must be on Qualified Product List for the Coating(905.03C1).

Or

- Test prior to incorporation.  One test per project per manufacturer.

Visual Inspection:  Maximum 500 pounds.

NOTE:  Pullout test required – Documentation placed in the Project Files.

Welded Wire Fabric

- General Certification from an Approved Manufacturer

Or

- Test prior to incorporation.  One test per project per manufacturer.

Visual Inspection: Maximum 500 square yards.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENCE ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements

6030040 – 6030053	PAVT REPAIR, NONREINF CONC, __ INCH

6030060 – 6030072	PAVT REPR, REINF CONC, __ INCH

Pg 4 of 4

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.  Refer to MDOT Construction Manual WIKI, or as superseded, for additional information.

- Form 1174R - Inspector’s Report of Concrete Placed - roadway.  One report per day of placement completely filled out. Document all underruns.

- Contractors QC documentation

Note: Refer to Standard Plan R-44

- Measurement and payment

- Engineer will measure based on pavement surface

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

6030095-6030096			SAWING AND SEALING PAVT JOINTS

6030100-6030101	RESEALING  JOINTS W/HOT POURED RUBBER

Pg 1 of 1 		Pay Unit:  Foot

MATERIALS:	Backer Rod, Hot Poured Joint Sealant

ACCEPTANCE TESTING REQUIREMENTS

Backer Rod

Visual Inspection:  All material placed.

Hot Poured Joint Sealant

- Per Special Provision 12SP914B

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure length of the joint.

7040001	STEEL SHEET PILING, PERMANENT

Pg 1 of 1	Pay Unit:  Square Foot

MATERIALS:	Steel Sheet Piling

ACCEPTANCE TESTING REQUIREMENTS

Steel Sheet Piling

- General Certification and Buy America Certification.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the United States.  It should be noted that this is different than the “BUY AMERICAN” statement which may also be listed.  “BUY AMERICAN” is not an acceptable alternate to “BUY AMERICA”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will calculate quantity based on the lines and lengths below cut off shown on the plans.

7040002	STEEL SHEET PILING, TEMP

7040003	STEEL SHEET PILING, TEMP, LEFT IN PLACE

Pg 1 of 1	Pay Unit:  Square Foot

MATERIALS:	Steel Sheet Piling

ACCEPTANCE TESTING REQUIREMENTS

Steel Sheet Piling

1.	Temporary Piling

a.	General Certification.

- Temporary Piling Left in Place

  - General Certification along with Buy America Certification

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will calculate quantity based on the area of earth retention.

3. Additional Documentation Requirements in project file

a.  Approved Shop Drawings and required Calculations

7050020	PILE, CIP CONC, FURN AND DRIVEN, 12 INCH

7050021	TEST PILE, CIP CONC, 12 INCH

7050025	PILE POINTS, CIP CONC

Pg 1 of 3	Pay Unit:  Foot, Each

MATERIALS:	Concrete Grade S1, Pile Points, Pile Shells

Note: Refer to 12SP604 for concrete QC/QA requirement

ACCEPTANCE TESTING REQUIREMENTS

Concrete Grade S1

NRMCA Plants

1.	Plant

- Current NRMCA certification.

2.	Scales Check

- Inspection certification every 6 months.

3.	Dispenser Check

- Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

- Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

Materials

1.	Cement

- General Certification from the Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse Aggregates

- Test prior to incorporation.  One test per 1,000 tons L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

Visual Inspection:  Maximum 100 tons for total grade used on job

7050020	PILE, CIP CONC, FURN AND DRIVEN, 12 INCH

7050021	TEST PILE, CIP CONC, 12 INCH

7050025	PILE POINTS, CIP CONC

Pg 2 of 3

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

Visual Inspection:  Maximum 100 tons for total FA used on job.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- GGBFS

- General Certification from the Approved Manufacturer

- Fly Ash

a.	General Certification from the Approved Manufacturer

- Liquid Concrete Admixtures

  - VI and must be on Qualified Product List (903.01, 903.02 & 903.03).

Foundation Piles and Points

- A Test Data Certification

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements

7050020	PILE, CIP CONC, FURN AND DRIVEN, 12 INCH

7050021	TEST PILE, CIP CONC, 12 INCH

7050025	PILE POINTS, CIP CONC

Pg 3 of 3

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.  Inspector Must sign all delivery tickets. Refer to MDOT Construction Manual WIKI, or as superseded, for additional information.

- Form 1174S - Inspector’s Report of Concrete Placed - structure.  One report per day of placement completely filled out. Document all underruns.

- Contractors QC documentation

- Need forms 1125, 1138, 1161 and 1157.

- Measurement and payment

- Test Piles - Department will pay for test piles in addition to the contract unit prices for furnished and driven pile pay items.

- Production Piles - Engineer will measure by the length of piling left in place below cut off.

- Pile Points – Engineer will base payment for each pile point used

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Additional Documentation Requirements in project file

- Need form 1157A and 1956

  - Approved welding plan and welding certifications for welders.

  - SP 705A, SP 705B, and SP 705C

7050030 & 7050034	PILES, STEEL  FURN AND DRIVEN, __ INCH

7050031 & 7050035	TEST PILES, STEEL ____ INCH

7050039	PILE POINT, STEEL___

Pg 1 of 1	Pay Unit:  Ea, Foot,

MATERIALS:	Steel Piles, Pile Points

ACCEPTANCE TESTING REQUIREMENTS

Steel Piles and Points

- A Test Data Certification

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Need form 1161 and 1157.

- Measurement and payment

- Test Piles - Department will pay for test piles in addition to the contract unit prices for furnished and driven pile pay items.

- Production Piles - Engineer will measure by the length of piling left in place below cut off.

- Additional Documentation Requirements in project file

- Need form 1157A and 1956

  - Approved welding plan and welding certifications for welders.

  - SP 705A and SP 705B

7060090	REINFORCEMENT, STEEL

Pg 1 of 1	Pay Unit:  Pound

MATERIALS:	Steel Reinforcement

ACCEPTANCE TESTING REQUIREMENTS

Steel Reinforcement

- A General Certification from the Approved Manufacturer.

Or

Test prior to incorporation.  One test per project per Manufacturer and per Size.

Visual Inspection: Maximum 500 pounds

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Form 1138 and 1125 needs to be turned in with the IDR.  Refer to MDOT Construction Manual WIKI for additional information.

- Measurement and payment

- Engineer will calculate the weight of the bar from the theoretical bar weight per table 706-2 of Standard Specifications.

7060092	REINFORCEMENT, STEEL, EPOXY COATED

Pg 1 of 1	Pay Unit:  Pound

MATERIALS:	Steel Reinforcement Epoxy Coated

ACCEPTANCE TESTING REQUIREMENTS

Steel Reinforcement Epoxy Coated

- A General Certification from the Approved Manufacturer for Bar

- A General Certification from the Approved Manufacturer for Coating Company.

- VI and must be on Qualified Product List for the Coating (905.03C1).

Or

- Test prior to incorporation.  One test per project per Manufacturer and per Size.

Visual Inspection: Maximum 500 pounds

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Form 1138 and 1125 needs to be turned in with the IDR.  Refer to MDOT Construction Manual WIKI, for additional information.

- Measurement and payment

- Engineer will calculate the weight of the bar from the theoretical bar weight per table 706-2 of Standard Specifications.

END OF DAY THREE

7060010 – 7060013	CONC, GRADE, __

7060100	SUBSTRUCTURE CONC

7060101	SUBSTRUCTURE CONC, HIGH PERFORMANCE

7060110	SUPERSTRUCTURE CONC

7060113	SUPERSTRUCTURE CONC, NIGHT CASTING

7060116	SUPERSTRUCTURE CONC, HIGH PERFORMANCE

7060117	SUPERSTRUCTURE CONC, NIGHT CASTING, HIGH PERFORMANCE

Pg 1 of 3	Pay Unit:  Cubic Yard

NOTES:	For Substructure and Superstructure Concrete refer to Construction Manual WIKI, or as superseded.  	Refer to 12SP604B, or as superseded, for concrete QC/QA requirement

MATERIALS:	Bituminized Fiber Joint Filler, Concrete Grade S2, S2M, T, DM, and D, Curing Compound, Hot Poured Rubber

ACCEPTANCE TESTING REQUIREMENTS

Bituminized Fiber Joint Filler

- A Test Data Certification

Or

- Test prior to incorporation.  One test per 1,000 square feet or fraction thereof.

Visual Inspection:  Maximum 150 square feet

Concrete Grade S2, S2M, T, DM, and D

NRMCA Plants

1.	Plant

a.	Current NRMCA certification.

2.	Scales Check

a.	Inspection certification every 6 months.

3.	Dispenser Check

a.	Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For Portable Batch Plants

1.	Plant

- Documentation of Inspection after each move per 601.03.A.1.b.  With Waiver certification per 601.03.C from the Engineer

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

- Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

7060010 – 7060013	CONC, GRADE, __

7060100	SUBSTRUCTURE CONC

7060101	SUBSTRUCTURE CONC, HIGH PERFORMANCE

7060110	SUPERSTRUCTURE CONC

7060113	SUPERSTRUCTURE CONC, NIGHT CASTING

7060116	SUPERSTRUCTURE CONC, HIGH PERFORMANCE

7060117	SUPERSTRUCTURE CONC, NIGHT CASTING, HIGH PERFORMANCE

Pg 2 of 3

Materials

1.	Cement

- Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse/Intermediate Aggregates

  - Test prior to incorporation.  One test per 1,000 tons.  Maximum VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons for total grade used on job

- Fine Aggregate

  - Test prior to incorporation.  One test per 1,000 tons.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons for total FA used on job

- Liquid Concrete Admixtures

a.	VI and must be on Qualified Products List (903.01, 903.02 & 903.03).

- GGBFS

  - Approved Manufacturer

- Fly Ash

  - Approved Manufacturer

7060010 – 7060013	CONC, GRADE, __

7060100	SUBSTRUCTURE CONC

7060101	SUBSTRUCTURE CONC, HIGH PERFORMANCE

7060110	SUPERSTRUCTURE CONC

7060113	SUPERSTRUCTURE CONC, NIGHT CASTING

7060116	SUPERSTRUCTURE CONC, HIGH PERFORMANCE

7060117	SUPERSTRUCTURE CONC, NIGHT CASTING, HIGH PERFORMANCE

Pg 3 of 3

Hot Poured rubber

- VI Per Special Provision 12SP914B

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load. The Engineer must collect, verify the mixture proportions (JMF) and record discharge time, and sign each concrete delivery ticket prior to discharge. Water additions must be noted.  Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174S - Inspector’s Report of Concrete Placed - structure.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Forms 1125 and 1131 wet and dry check to be completed by inspection

- Form 2082 to be started by the inspector

- Contractors QC documentation

- Measurement and payment

  - Concrete Grade S2, S2M, T, DM, and D – The Engineer will calculate and pay quantities for pay items based on the lines and dimensions shown on the plans.

  - Superstructure – The Engineer will measure superstructure concrete for decks based on batch plant tickets with deductions made for material wasted or rejected.

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

7060140	WATER REPELLENT TREATMENT, PENETRATING

Pg 1 of 1	Pay Unit:  Square Yard

MATERIALS:	Penetrating Water Repellents

ACCEPTANCE TESTING REQUIREMENTS

Penetrating Water Repellents

- VI of the Qualified Products List (706.03S).

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- The Engineer will calculate and pay quantities for pay items based on the lines and dimensions shown on the plans.

7070050 - 7070071	Structural Steel, Mixed, Erect

Pg 1 of 1	Structural Steel, Mixed, Furn and Fab

Structural Steel, Plate, Erect

Structural Steel, Plate, Furn and Fab

Structural Steel, Rolled Shape, Erect

Structural Steel, Rolled Shape, Furn and Fab

Pay Unit:  Pound

MATERIALS:	High Strength Bolts, Nuts and Washers, Structural Steel__,

ACCEPTANCE TESTING REQUIREMENTS

High Strength Bolts, Nuts and Washers

- Need to be tested.

Structural Steel

- Fabrication inspection documents, According to MQAP manual section 4.05, and Elements will be stamped or tagged “Approved for Use” by the QA shop inspector.

- LAPs are responsible for all testing requirements.

NOTE:  Local Government Agency is required to hire independent agency to perform all
required testing. Reports must be signed by inspector performing the testing and/or inspection.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials must be stamped approved before incorporation and must be VI and accepted by the inspector with notation on the IDR.

- Ensure bolts are tightened and document on IDR per section 707.03.D.7.c

- Stamped Bill of Lading Must be collected at time of delivery, scanned and placed in ProjectWise

- When item is completed FFM (Final Field Measurement) will be based on approved pay weights.

- Measurement and payment

- The Engineer will measure structural steel by the calculated weight of metal in the finished structure excluding filler material in welding (Approved Pay Weights) per section 707.04 of the Standard Specification.

Additional Requirements

- Need approved shop drawings

- MDOT Field Welding Plans (Form 0394 and 0395) are required to be approved by Operations Field Services – Structural Fabrication Unit.  Field welders must be endorsed by MDOT for the field welding taking place in accordance with MDOT’s Welder Certification Program or MDOT's Welder Qualification Program.

- See current special provisions 12SP-707A (Structural Steel and Aluminum Construction), 12SP-707B, and 12SP-707F (Structural Steel Construction Revisions) for additional construction requirements.

7070010 – 7070024	BEARING, ELASTOMERIC, __ INCH

Pg 1 of 1	Pay Unit:	Square Inch

MATERIALS:	Elastomeric Bearing Pads

ACCEPTANCE TESTING REQUIREMENTS

Elastomeric Bearing Pads

- A Test Data Certification.  Show test result for Shear Modulus, ASTM D 4014.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

  - Engineer will measure, with no deduction for holes.

7070040	SHEAR DEVELOPERS

Pg 1 of 1	Pay Unit:	Lump Sum

MATERIALS: 	Shear Developers

ACCEPTANCE TESTING REQUIREMENTS

Shear Developers

- VI of the Qualified Products List (906.09).

Note on Testing Studs

1.	Studs are tested by ringing with a hammer.  To test the studs, the inspector should allow studs to cool before testing.  The first two studs welded will be bent to a 30 degree angle without breaking the weld.  If the weld breaks, repairs will be made and the next set of studs tested along with the studs that were repaired.  The rest of the studs on that beam can then be checked for proper welding.  Sufficient tests should be made to insure proper procedures are being followed (bend over additional studs).  If a weld defect is found, the stud may be bent to an angle of 15 degrees away from the defect.  If no weld break occurs, the stud is acceptable.  No welding will be done when the temperature of the base material is below 32 degrees F (0 degrees C) or when the surface is wet or exposed to rain or snow.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure as a unit for each structure.

7080001 - 7080010	PREST CONC DECK, __ INCH

Pg 1 of 3 	Pay Unit:	Square Foot

MATERIALS:	Concrete, Precast Panels

ACCEPTANCE TESTING REQUIREMENTS

Precast Panels

- Fabrication inspection documents, According to MQAP manual section 4.04, and Elements will be stamped or tagged “Approved for Use” by the QA shop inspector.

- LAP are responsible for all testing requirements.

NOTE:  Local Government Agency is required to hire independent agency to perform all
required testing. Reports must be signed by QA inspector performing the testing and/or inspection.

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials must be stamped approved before incorporation and must be VI and accepted by the inspector with notation on the IDR.

- Stamped Bill of Lading Must be collected at time of delivery, scanned and placed in ProjectWise

Measurement and payment

- Engineer will measure based on the nominal overall length of the units, multiplied by the overall plan width.

Additional Requirements

- Need approved shop drawings

- See current special provisions 12SP-708A and 12SP-708C for additional construction requirements.

7080015	POST TENSIONING, (STRUCTURE NO.)

Pg 1 of 1	Pay Unit:	Lump Sum

MATERIALS:	Grout E-1, Post Tensioning Strands (Tendons)

ACCEPTANCE TESTING REQUIREMENTS

Grout E-1

      - Test Data Certification

Post Tensioning Strands (Tendons)

- Strands

- A General Certification from an Approved Manufactures.

NOTE:	Sampling and testing may be waived if strand from same reel is tested for beam fabrication.

NOTE: Visual Inspection:  	All material placed.  Verify mix proportioning per Standard

Specifications table 702.1A and 702.1B.

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Test for slump and air when required.

- Measurement and payment

- Engineer will pay as Lump Sum per structure number

7080021 – 7080041	PREST CONC I BEAMS, __, __ INCH

7080051 – 7080096	PREST CONC BOX BEAM, __, __ INCH

7080101 – 7080102	PREST CONC 1800  BEAM, __

7080110 – 7080176	PREST CONC Bulb-Tee Beam, __ INCH

Pg 1 of 2	Pay Unit:	Foot

MATERIALS:	Prest Concrete Beams

ACCEPTANCE TESTING REQUIREMENTS

Prest Concrete Beams

- Fabrication inspection documents, According to MQAP manual section 4.04, and Elements will be stamped or tagged “Approved for Use” by the QA shop inspector.

- LAP are responsible for all testing requirements.

NOTE:  Local Government Agency is required to hire independent agency to perform all
required testing. Reports must be signed by QA inspector performing the testing and/or inspection.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Notation on IDR confirming the fabrication acceptance stamp on beams.

- Stamped Bill of Lading Must be collected at time of delivery, scanned and placed in ProjectWise.

- Measurement and payment

- Engineer will measure based on the nominal length of the unit.

Additional Requirements

- Need approved shop drawings

- See current special provisions 12SP-708A 12SP-708B and 12SP-708C for additional construction requirements.

7100001	JOINT WATERPROOFING

Pg 1 of 1 	Pay Unit:	Square Foot

MATERIALS:	Waterproofing Membrane - Preformed

ACCEPTANCE TESTING REQUIREMENTS

Waterproofing Membrane - Preformed

- VI of the Qualified Products List (914.11).

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure based on width of 18 inch and the plan length of the joint.

7110005	BRIDGE RAILING, AESTHETIC PARAPET TUBE

Pg 1 of 3	Pay Unit:	Foot

MATERIALS:	Anchor Studs, Concrete - Grade D & DM, Curing Compound
High Strength Bolts, Tubing, Steel Railing

ACCEPTANCE TESTING REQUIREMENTS

Anchor Studs

- Test.  One test per heat per diameter per project.

Concrete - Grade D

NRMCA Plants

1.	Plant

a.	Current NRMCA certification.

2.	Scales Check

a.	Inspection certification every 6 months.

3.	Dispenser Check

a.	Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For non NRMCA Plants:  All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

a.	Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

Materials

1.	Cement

- Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse Aggregates

- Test prior to incorporation.  One test per 1,000 tons L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

Visual Inspection:  Maximum 100 tons for total grade used on job

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

Visual Inspection:  Maximum 100 tons for total FA used on job.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- GGBFS

- Approved Manufacturer

- Fly Ash

- Approved Manufacturer

- Liquid Concrete Admixtures

a.	VI and must be on Qualified Products List (903.01, 903.02 & 903.03).

Curing Compound

- A Test Data Certification.  One test per lot or batch.

Visual Inspection:  Maximum 200 gallons.

NOTE:  Must be used within one year of manufacturer date.

High Strength Bolts

- Test.  One test per heat per diameter per project

NOTE:  Standard Plan B-25-Series.

Tubing, Steel Railing

- MDOT gets Memo to file for Fabrication inspection, Shop inspection of structural steel reports (Form 538). According to MQAP manual section 4.05 and  SP 12SP707B.

- LAP needs Fabrication inspection, Shop inspection of structural steel reports (Form 0538), Buy America certification, and According to MQAP manual section 4.05 in the project file.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

7110005	BRIDGE RAILING, AESTHETIC PARAPET TUBE

Pg 3 of 3

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Inspector Must sign all delivery tickets, Water additions must be noted.   Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174S - Inspector’s Report of Concrete Placed - structure.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Notation on IDR confirming the fabrication acceptance stamp on Tube Railing.

- Stamped Bill of Lading Must be collected at time of delivery, scanned and placed in ProjectWise

- Contractors QC documentation

- Measurement and payment

- Engineer will measure based on Plan Quantity

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

7120010	PATCH, FULL DEPTH

7120015 - 7120016	PATCHING MORTAR OR CONC

7120110 - 7120115		PATCHING CONC, C; C-HE; C-L; C-L-HE; F-L; M

Pg 1 of 3 	Pay Units:	Cubic Foot, Cubic Yard

MATERIALS:	Concrete – Grade C, C-HE, M, Curing Compound,
and Structure Patching Mixture (Conc C; C-HE; C-L; C-L-HE; F-L; M)

ACCEPTANCE TESTING REQUIREMENTS

Concrete - Grade C; C-HE; M

NRMCA Plants

1.	Plant

a.	Current NRMCA certification.

2.	Scales Check

a.	Inspection certification every 6 months.

3.	Dispenser Check

a.	Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For non NRMCA Plants:  All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

a.	Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

Materials

- Cement

- Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse Aggregates

- Test prior to incorporation.  One test per 1,000 tons L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

Visual Inspection:  Maximum 100 tons for total grade used on job

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

7120010	PATCH, FULL DEPTH

7120015 - 7120016	PATCHING MORTAR OR CONC

7120110 - 7120115		PATCHING CONCRETE, C; C-HE; C-L; C-L-HE; F-L; M

Pg 2 of 3

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

Visual Inspection:  Maximum 100 tons for total FA used on job.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

- GGBFS

- Approved Manufacturer

- Fly Ash

- Approved Manufacturer

- Liquid Concrete Admixtures

- VI and must be on Qualified Products List (903.01, 903.02 & 903.03).

Curing Compound

- A Test Data Certification.  One test per lot or batch.

Visual Inspection:  Maximum 200 gallons.

NOTE:  Must be used within one year of manufacturer date.

Structural Patching Mixture(Conc C; C-HE; C-L; C-L-HE; F-L; M)

- Portable Mixing Truck

  - Provide annual certification to the engineer or demonstrate by field test, the equipment is calibrated for yield and proportioning.

  - Delivery tickets

  - Latex admixture – Approved Manufacture and General Certification

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements

7120010	PATCH, FULL DEPTH

7120015 - 7120016	PATCHING MORTAR OR CONC

7120110 - 7120115		PATCHING CONCRETE, C; C-HE; C-L; C-L-HE; F-L; M

Pg 3 of 3

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Form 1174S - Inspector’s Report of Concrete Placed - structure.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Measurement and payment

- Engineer will measure based on volume in-place.

Note: Patch, Full Depth in conjunction with overlay, the Department will only pay for patching the area shown on the plans.

- Additional Documentation Requirements in project file

- Work progress specimen if necessary

- Alkali – Silica Reactivity (ASR) test report per special provision.

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

7120028 – 7120038	ADHESIVE ANCHORING OF __ BAR, __ INCH

7120040 – 7120044	BOLT, ADHESIVE ANCHORED, __ INCH

7120050 – 7120052	BOLT, Mechanical EXPANSION ANCHORED,__ INCH

Pg 1 of 1 	Pay Unit:	Each

MATERIALS:	Adhesive System, Bolts

ACCEPTANCE TESTING REQUIREMENTS

Adhesive System

- VI of the Qualified Products List (712.03J).

Bolts

- Test One bolt per diameter/heat/per project.  A Test Data Certification must be submitted with sample for testing.

Structure Expansion Anchored (Mechanical Expansion Anchored)

- VI of the Qualified Products List (712.03K).

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

Pull-Out Testing

- Field Inspection Report (see form 0566).  See subsection 712.03.J.

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure based on each item placed.

7120084	REINFORCEMENT, MECHANICAL SPLICE

Pg 1 of 1 	Pay Unit:	Each

MATERIALS:	Reinforcement Mechanical Splice

ACCEPTANCE TESTING REQUIREMENTS

Reinforcement Mechanical Splice

- VI of the Qualified Products List (712.03L).

- Test – The contractor must make test splices, witnessed by the Engineer, on the largest bar size being spliced.

- Mechanical and other splices:  Make two test splices on the largest bar size being spliced.  Test splice consists of 2 pieces of reinforcing bar joined by the coupler with a minimum of 12 inches or bar exposed on each end of the coupler.

NOTE: Use these tests to establish a splicing procedure. Demonstrate that splices have a tensile strength of 125 percent of the bar’s yield strength.  For all required tests, supply sample bars with 12 inches of exposed bar on each end.  If the existing reinforcing steel being spliced has an inferior or badly corroded exterior deformation pattern, the Engineer may require additional qualification testing on these bars.  The Department will test all test splices.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

- Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure based on each item placed.

7150045	STEEL STRUCTURES CLEANING, TYPE 4

Pg 1 of 1	Pay Unit:	Lump Sum

MATERIALS:	Low Dusting Abrasive, Steel Grit/Shot

Note: Refer to Construction Manual WIKI and 12SP-715B in proposal

ACCEPTANCE TESTING REQUIREMENTS

Low Dusting Abrasive

- VI of the Qualified Products List (715.02).

Steel Grit/Shot

- VI

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Form 1941 to be completed by the Inspector.

- Form 2081 started in the Field by the inspector

- Measurement and payment.

- Engineer will measure as a unit for each structure.

7150046	STEEL STRUCTURE, COATING, TYPE 4

Pg 1 of 1 	Pay Unit:	Lump Sum

MATERIALS:	Coating System

Note: Refer to Construction Manual WIKI and 12SP-715A in proposal

ACCEPTANCE TESTING REQUIREMENTS

Coating System

- VI of the Qualified Products List (915).

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Form 1941 completed by the inspector.

- Form 2081 started in the Field by the inspector.

- Measurement and payment.

- Engineer will measure as a unit for each structure.

8010001 – 8010004	DRIVEWAY, REINF CONC, __INCH

8010005 – 8010008	DRIVEWAY, NONREINF CONC, __ INCH

Pg 1 of 4	Pay Unit:  Square Yard

MATERIALS:	Bituminous Fiber Filler, Concrete Grade P1, P-NC and S2,

Curing Compound-White, Wire Fabric

Note: Refer to 12SP-604 B for concrete QC/QA requirement

ACCEPTANCE TESTING REQUIREMENTS

Bituminized Fiber Joint Filler

- A Test Data Certification.

Visual Inspection:  Maximum 150 square feet for all other sizes.

Concrete Grade P1, P-NC, S2

NRMCA Plants

1.	Plant

a.	Current NRMCA certification.

2.	Scales Check

a.	Inspection certification every 6 months.

3.	Dispenser Check

a.	Inspection certification every 90 days.

- Concrete Mix Design

  - Form 1976 in project files

For Portable Batch Plants

1.	Plant

  - Documentation of Inspection after each move per 601.03.A.1.b.  With Waiver certification per 601.03.C from the Engineer

For non NRMCA Plants: All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

1.	Scales Check

a.	Inspection certification every 6 months

2.	Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Form 1976 in project files

8010001 – 8010004	DRIVEWAY, REINF CONC, __INCH

8010005 – 8010008	DRIVEWAY, NONREINF CONC, __ INCH

Pg 2 of 4

Materials

1.	Cement

  - Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse/Intermediate Aggregates

- Test prior to incorporation.  One test per 1,000 tons.  Max. VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons for total grade used on job

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

- See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons for total FA used on job

- Liquid Concrete Admixtures

VI and must be on Qualified Products List (903.01, 903.02 & 903.03).

- GGBFS

- Approved Manufacturer

- Fly Ash

  - Approved Manufacturer

8010001 – 8010004	DRIVEWAY, REINF CONC, __INCH

8010005 – 8010008	DRIVEWAY, NONREINF CONC, __ INCH

Pg 3 of 4

Curing Compound

- A Test Data Certification.  One test per lot or batch.

Visual Inspection:  Maximum 200 gallons

NOTE: Must be used within one year of manufacturer date.

Wire Fabric

- A General Certification from an Approved Manufacturer

Or

- Test prior to incorporation.  One test per project per manufacturer.

Visual Inspection:  Maximum 500 square yards.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

  - All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.   Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174R - Inspector’s Report of Concrete Placed - roadway.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Contractors QC documentation.

- Measurement and payment

- Engineer will measure quantity based on surface area in place.

8010001 – 8010004	DRIVEWAY, REINF CONC, __INCH

8010005 – 8010008	DRIVEWAY, NONREINF CONC, __ INCH

Pg 4 of 4

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

END  of  Day FOUR

8020001 – 8020006	Curb, Conc, Det __

8020010	Curb and Gutter, Bridge Approach

8020015 – 8020040	Curb and Gutter, Conc, Det __

Pg 1 of 4	Pay Unit:	Foot

MATERIALS:	Bituminous Fiber Filler, Concrete Grade P1 and S2,

Curing Compound-White, Lane Ties Bars,

Mortar Standard, Steel Reinforcement-Epoxy Coated

ACCEPTANCE TESTING REQUIREMENTS

Bituminized Fiber Joint Filler

- A Test Data Certification.

Visual Inspection:  Maximum 150 square feet.

Concrete Grade P1, S2

NRMCA Plants

- Plant

a.	Current NRMCA certification

- Scales Check

- Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

- Copy in project files

For Portable Batch Plants

1.	Plant

  - Documentation of Inspection after each move per 601.03.A.1.a.

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

- Scales Check

  - Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Copy in project files

8020001 – 8020006	Curb, Conc, Det __

8020010	Curb and Gutter, Bridge Approach

8020015 – 8020040	Curb and Gutter, Conc, Det __

Pg 2 of 4

Materials

- Cement

- Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse/Intermediate Aggregates

- Test prior to incorporation.  One test per 1,000 tons.  Max. VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons

- Liquid Concrete Admixtures

- VI and must be on Qualified Products List (903.01, 903.02 & 903.03).

- GGBFS

- Approved Manufacturer

- Fly Ash

- Approved Manufacturer

8020001 – 8020006	Curb, Conc, Det __

8020010	Curb and Gutter, Bridge Approach

8020015 – 8020040	Curb and Gutter, Conc, Det __

Pg 3 of 4

Curing Compound

- A Test Data Certification.

Visual Inspection:  Maximum 200 gallons

NOTE: Must be used within one year of manufacturer date.

Lane Tie Bars

- A General Certification from the Approved Manufacturer for Bar

- A General Certification from the Approved Manufacturer for Coating Company

- VI and must be on Qualified Products List for coating (905.03C1).

Visual Inspection:  Maximum 500 pounds

Mortar Standard

      - Visual Inspected

Steel Reinforcement Epoxy Coated

- A General Certification from the Approved Manufacturer for Bar

- A General Certification from the Approved Manufacturer for Coating Company

- VI and must be on Qualified Products List for coating (905.03C1).

Visual Inspection:  Maximum 500 pounds

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

8020001 – 8020006	Curb, Conc, Det __

8020010	Curb and Gutter, Bridge Approach

8020015 – 8020040	Curb and Gutter, Conc, Det __

Pg 4 of 4

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

  - All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.   Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174R - Inspector’s Report of Concrete Placed - roadway.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Contractors QC documentation

Note: Standard Plans R-27, R-30, R-31, R-32, and R-33

- Measurement and payment

- Engineer will measure in place along the joint of the curbing with the pavement.

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Local Agency Projects

Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

8030030	Curb Ramp Opening, Conc

8030033 - 8030037	SIDEWALK RAMP

8030043 – 8030047	SIDEWALK, CONC, __ INCH

Pg 1 of 3	Pay Unit:	Foot, Square Foot

MATERIALS	Bituminous Fiber Filler, Concrete Grade P1, P2, S2 and S3,

Curing Compound-White, Granular Material Cl II

Note: Refer to SP 604 B for concrete QC/QA requirement

ACCEPTANCE TESTING REQUIREMENTS

Bituminized Fiber Joint Filler

- A Test Data Certification from the Approved Manufacturer.

Visual Inspection:  Maximum 150 square feet for all other sizes.

Concrete Grade P1, P2, S2, S3

NRMCA Plants

- Plant

a.	Current NRMCA certification

- Scales Check

- Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

- Copy in project files

For Portable Batch Plants

1.	Plant

  - Documentation of Inspection after each move per 601.03.A.1.a.

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

- Scales Check

  - Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Copy in project files

8030030	Curb Ramp Opening, Conc

8030033 - 8030037	SIDEWALK RAMP

8030043 – 8030047	SIDEWALK, CONC, __ INCH

Pg 2 of 3

Materials

- Cement

- Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

- Coarse/Intermediate Aggregates

  - Test prior to incorporation.  One test per 1,000 tons.  Max. VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons

- Fine Aggregate

  - Test prior to incorporation.  One test per 1,000 tons.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons

- Liquid Concrete Admixtures

- VI and must be on Qualified Products List (903.01, 903.02 & 903.03).

- GGBFS

  - Approved Manufacturer

- Fly Ash

  - Approved Manufacturer

Curing Compound

- A Test Data Certification.

Visual Inspection:  Maximum 200 gallons

NOTE: Must be used within one year of manufacturer date.

8030030	Curb Ramp Opening, Conc

8030033 - 8030037	SIDEWALK RAMP

8030043 – 8030047	SIDEWALK, CONC, __ INCH

Pg 3 of 3

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

- See Notes page for IAT requirements

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

  - All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.   Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174R - Inspector’s Report of Concrete Placed - roadway.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Contractors QC documentation.

Note: Standard Plans R-28 and R-29 and Special Provision 12SP803B

- Measurement and payment

- Engineer will measure in place area.

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

- Local Agency Projects

- Refer to 12SP604A (or as superseded) QUALITY CONTROL AND ACCEPTANCE OF PORTLAND CEMENT CONCRETE (FOR LOCAL AGENCY PROJECTS ONLY).

- Density Reports

  - Density testing as per subsection 302.03 of the standard specifications.

NOTE:

All density reports are to be placed in ProjectWise  on a daily basis, and must be sent weekly to the Area Density Specialist and the Lansing Density Technology Unit at a minimum. Field staff must perform moisture checks on weight pay items and note the value on the IDRs.

8070000 – 8070009	GUARDRAIL, TYPE __

8070010 – 8070012	GUARDRAIL, CURVED, TYPE __

Page 1 of 2 	Pay Unit:	Foot

MATERIALS:	Blocks (Plastic or Wood), Guardrail Beam Elements and Hardware (includes all components from same manufacturer), Wood Post

ACCEPTANCE TESTING REQUIREMENTS

Blocks (Plastic or Wood)

- VI and must be on Qualified Products List for Plastic Block (912.09Q).

- Wood –

a. A General Certification from the Approved Manufacturer.

Or

  - Test prior to incorporation.  One test per charge.

Guardrail Beam Element and Hardware

- A General Certification from the Approved Manufacturer.

Or

- Test prior to incorporation.  Beam element - One test per project per manufacturer.

Visual Inspection: 	Maximum VI for beam elements 125 feet

Maximum VI for steel post 25 Each.

Wood Post

- A General Certification from the Approved Manufacturer.

Or

- Test prior to incorporation.  One test per charge.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

8070000 – 8070009	GUARDRAIL, TYPE __

8070010 – 8070012	GUARDRAIL, CURVED, TYPE __

Page 2 of 2

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR .

Note: Standard Plans R-59, R-60, R-73 and Special Detail 21.

- Measurement and payment

- Engineer will measure along the face of the rail.

8070020 – 8070033		GUARDRAIL ANCHORAGE, BRIDGE, DETAIL __

Pg 1 of 2	Pay Unit:	Each

MATERIALS:	Blocks (Plastic or Wood), Guardrail Beam Elements and Hardware (includes all components from same manufacturer), Wood Post

ACCEPTANCE TESTING REQUIREMENTS

Blocks (Plastic or Wood)

- VI and must be on Qualified Product List Plastic Blocks(912.09Q).

- Wood

A General Certification from the Approved Manufacturer

Or

- Test prior to incorporation.  One test per charge.

Guardrail Beam Element and Hardware

- A General Certification from the Approved Manufacturer.

Or

- Test prior to incorporation.  Beam element - One test per project per manufacturer.

Visual Inspection:	Max VI for beam elements 125 feet

Max VI for steel post 25 Each.

Wood Post

- A General Certification from the Approved Manufacturer.

Or

- Test prior to incorporation.  One test per charge.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

8070020 – 8070033		GUARDRAIL ANCHORAGE, BRIDGE, DETAIL __

Pg 2 of 2

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Standard Plan R-67

- Measurement and payment

- Engineer will measure each item in-place.

8070080	GUARDRAIL REFLECTOR

Pg 1 of 1 	Pay Unit:	Each

MATERIALS:	Reflectorized Washer

ACCEPTANCE TESTING REQUIREMENTS

Reflectorized Washer

- VI on IDR.  Inspect galvanizing, dimensions and type of sheeting.

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will measure each item in-place.

8070095	POST, MAILBOX

Pg 1 of 1 	Pay Unit:	Each

MATERIALS:	Wood Post

ACCEPTANCE TESTING REQUIREMENTS

Wood Post

- Visual Inspection

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Measurement and payment

- Engineer will measure each item in-place

8080001	FENCE, WOVEN WIRE WITH WOOD POST

8080002	FENCE, WOVEN WIRE WITH STEEL POSTS

Pg 1 of 3 	Pay Unit:	Foot

MATERIALS:	Barbed Wire, Concrete Grade P2, Steel Post, Wood Posts,

Woven Wire Fabric and Hardware

ACCEPTANCE TESTING REQUIREMENTS

Barbed Wire

- VI along with BUY AMERICA statement required.  Document source on IDR.

Concrete Grade  P2

NRMCA Plants

- Plant

a.	Current NRMCA certification

- Scales Check

- Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

- Copy in project files

For Portable Batch Plants

1.	Plant

  - Documentation of Inspection after each move per 601.03.A.1.a.

For non NRMCA Plants

All of the following documentation is required including FORM 1174 CONCRETE PLANT PROPORTIONING (a minimum of one report per mix).

- Scales Check

  - Inspection certification every 6 months

- Dispenser Check

- Inspection certification every 90 days

- Concrete Mix Design

  - Copy in project files

Materials

1.	Cement

- Approved Manufacturer.

Visual Inspection:  Maximum 45 tons

8080001	FENCE, WOVEN WIRE WITH WOOD POST

8080002	FENCE, WOVEN WIRE WITH STEEL POSTS

Pg 2 of 3

- Coarse/Intermediate Aggregates

- Test prior to incorporation.  One test per 1,000 tons.  Max. VI 100 tons for total grade used on job.  L.A. Abrasion, freeze-thaw durability may be request from MDOT CFS.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons

- Fine Aggregate

- Test prior to incorporation.  One test per 1,000 tons.

b.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

Visual Inspection:  Maximum 100 tons

- Liquid Concrete Admixtures

- VI and must be on Qualified Products List (903.01, 903.02 & 903.03).  .

- GGBFS

- Approved Manufacturer

- Fly Ash

- Approved Manufacturer

Steel Post

- Test Data Certification .

Woven Wire Fabric and Hardware

- Test Data Certification.

8080001	FENCE, WOVEN WIRE WITH WOOD POST

8080002	FENCE, WOVEN WIRE WITH STEEL POSTS

Pg 3 of 3

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

Wood Post

Visual Inspection

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

  - All materials used must be VI and accepted by the inspector with notation on the IDR.

- Signed certification statement and batch weights required on each concrete delivery tickets from supplier for each load.  Water additions must be noted and signed.   Refer to MDOT Construction Manual WIKI, for additional information.

- Form 1174R - Inspector’s Report of Concrete Placed - roadway.  One report per day of placement completely filled out and name of inspector is required. Document all underruns.

- Contractors QC documentation

Note: Standard Plans R-101 and R-102

- Measurement and payment

- Engineer will measure fence in place and will not include gate openings and the measurement.

- Additional Documentation Requirements for Redi-mix concrete.

- Approved Contractor’s QC Plan per the Current 12SP604B, prior to work.

- Form 1155 the weekly summary of concrete shipped (for Regions who use numbered concrete plants).  Emailed or Fax copy to Regional CFS office.

- Approved QA Plan

- QA – Compressive Test reports for 28 day strength (work sheet not summary) per Department’s latest QA testing requirements.  Testers’ signature required.

- Attach pavement core thickness forms and document on IDR whether a penalty was required.

- Pull out test for lane ties required per section 602.03.F.2

- QA and QC Optimized aggregate test reports as required per the Materials Quality Assurance Procedures Manual 4.13.

8100370 - 8100371	POST, STEEL, __ LB

Pg 1 of 1 	Pay Unit:	Foot

MATERIALS:	Steel post

ACCEPTANCE TESTING REQUIREMENTS

Steel Post

- A Test Data Certification.

Visual Inspection:  Maximum 20 posts

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR .

- Measurement and payment

- Engineer will measure Sign Supports to the nearest commercial length required.

8100392 – 8100414 		SIGN, TYPE __

Pg 1 of 1 	Pay Unit:	Square Foot

MATERIALS:	Reflective Sheeting, Sign-Type I, III, IV, Sign-Type II.

ACCEPTANCE TESTING REQUIREMENTS

Reflective Sheeting

- VI and must be on Qualified Products List (919.02B1).

Sign, Type I, III, IV, V_

- Shipment of Tested Stock Report, Form 1922.

Visual Inspection:  Maximum 100 square feet (Type III, IV and V)

Sign, Type II

- General Certification must be attached and inspected at project site.

AND

- Grade mark on materials serves as certification

Sign Hardware

- General Certification

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Measurement and payment

- Engineer will measure Sign Supports to the nearest commercial length required.

8110022 – 8110295	PAVEMENT MARKINGS

Pg 1 of 1 	Pay Unit:	Foot & Each

MATERIALS:	Cold Plastic, Glass Beads, Polyurea, Regular Dry, Sprayable, Thermoplastic, Thermoplastic, Waterborne, Wet Reflective Beads/Elements

ACCEPTANCE TESTING REQUIREMENTS

Cold Plastic

- VI and must be on Qualified Products List

Glass Beads

- General Certification.

Visual Inspection:  Maximum 500 pounds.

Polyurea

- VI and must be on Qualified Products List (811.0D3).

Regular Dry

- VI and must be on Qualified Products List (811.0D2).

Sprayable Thermoplastic

- VI and must be on Qualified Products List (811.03D6).

Thermoplastic

- VI and must be on Qualified Products List (811.03D4).

Waterborne

- VI and must be on Qualified Products List (811.0D1).

Wet Reflective Beads/Elements

      - VI and must be on Qualified Products List

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Sample plates are required for All Permanent Liquid Applied Pavement Marking see the MDOT Construction Manual WIKI section 811, for the most updated sample frequency.

- 1585 is required one per project per season.

- Measurement and payment

- Engineer will verify the measured Pavement Markings.

8120080 – 8120083	CONC BARRIER, TEMP, __

Pg 1 of 1 	Pay Unit:	Foot

MATERIALS	Barrier Reflective Markers Temporary, Concrete Barrier

ACCEPTANCE TESTING REQUIREMENTS

Barrier Reflective Markers Temporary

      - General Certification per MQAP 4.10

Concrete Barrier

- A Test Data Certification from contractor, and Meets 922.04.A of the Standard Specification for Construction 2012.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Document the barrier wall meet ATSSA standard as shown in Latest Edition

  - Check for fully engaged connection between sections.

Note: Refer to Standard Plan R-126

- Measurement and payment

- Engineer will measure in-place at initial location with barrier reflector marker attached.

8120100	DUST PALLATIVE, APPLIED

Pg 1 of 1 	Pay Unit:	Ton

MATERIALS	Calcium Chloride Solids, Calcium Chloride Solutions

ACCEPTANCE TESTING REQUIREMENTS

Calcium Chloride Solutions

- Test Data Certification.  Load ticket or bag count required.

Visual Inspection:

1000 gals

Calcium Chloride Solids

- Test Data Certification.  Load ticket or bag count required.

Visual Inspection:

5000 lbs

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: see section 922.12 of the Standard Specifications for Construction 2012.

- Immediate possession of delivery tickets or shipping document is required.

- Measurement and payment

  - Engineer will pay based on weight of calcium chloride.

8120200		Pavt Mrkg cover, Type R, Black

8120215 – 8120246	PAVT MRKG, TYPE R AND PAVT MRK, TYPE NR

8120255 – 8120259	PavtMrkg, WtRef, Type R, Tape

Pg 1 of 1 	Pay Unit:	Foot

MATERIALS:	Glass Beads, Temp Pavement Marking Tape,

Temp Pavement Marking Paint, Wet Reflective Beads/Elements

ACCEPTANCE TESTING REQUIREMENTS

Glass Beads

- A General Certification.

Visual Inspection:  Maximum 500 pounds.

Temp Pavement Marking Paint

- VI and must be on Qualified Products List (811.03).

Temp Pavement Marking Tape

- VI and must be on Qualified Products List (922.06A).

Wet Reflective Beads/Elements

      - VI and must be on Qualified Products List

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Type R – Engineer will pay based on each unit placed and includes the cost of providing, installing, maintaining, removing and disposing of raised pavement markers.

- Type NR Tape and Paint - Engineer will pay based on each unit placed and includes the cost of providing and placing temporary pavement markings.

8120280 – 8120301	RAISED PAVT MRK, TEMP, TYPE __,

Pg 1 of 1	(COLOR), (DIRECTION)

Pay Unit:	Each

MATERIALS:	Temp Raised Pavement Marker

ACCEPTANCE TESTING REQUIREMENTS

Temp Raised Pavement Marker

- VI and must be on Qualified Products List (922.06B).

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR

- Measurement and payment

- Engineer will pay based on each unit placed and includes the cost of providing, installing, maintaining, removing and disposing of raised pavement markers.

8120250 -- 8120261	Plastic Drums, _____, ____

8120340 – 8120341	Sign, Type A, Temp, Prismatic, ___

8120350 -- 8120351	Sign, Type B, Temp, Prismatic, ___

8120352 -- 8120353	Sign, Type B, Temp, Prismatic, Special,  __

Pg 1 of 1 	Pay Unit: Each and Sft

MATERIALS	Plastic Drums, Sign Temporary Prismatic

ACCEPTANCE TESTING REQUIREMENTS SP 105 B

No Materials Source List required

Plastic Drums

      - General Certification per MQAP 4.10

Sign Temporary Prismatic

General Certification per MQAP 4.10,

Note:

Hyperlinks in the Crash Worthy Certification letter from contractor must work, taking you to ProjectWise Certification Documents

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Document that the devices meet ATSSA standard as shown in Latest Edition

- Measurement and payment

1   The Engineer will measure Sign, Type __, Temp, Prismatic, __ as the total area of the maximum number of signs with dissimilar sign legends in use, at one time on the project.

2. The Engineer will count Plastic Drums as the maximum number in use, at one time on the project.

8130005 – 8130012	RIPRAP, ___

Pg 1 of 1 	Pay Unit:	Square Yard, Cubic Yard or Ton

`

MATERIALS:	Geotextile Liner, Riprap

ACCEPTANCE TESTING REQUIREMENTS

Geotextile Liner

- Test as follows:

- Plain Riprap:  1 test from 500 to 1500 Syd, additional tests every 5,000 Syd.

- Heavy Riprap:  1 test from 500 to 1500 Syd, additional tests every 4,000 Syd.

Visual Inspection:  Maximum 500 square yards.

Riprap

- VI - Check special provision.  Load tickets are required if paying by Ton.  Document quantity used on IDR.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Riprap (Cyd) – Engineer will pay based on measured in-place volume.

- Riprap (Syd) – Engineer will pay based on measured in-place quantity.

- Riprap (Ton) - Engineer will pay based on weight.

8160020 – 8160022	FERTILIZER, CHEMICAL NUTRIENT, CL __

Pg 1 of 1	Pay Unit:	Pound

MATERIALS:		Chemical Fertilizer

ACCEPTANCE TESTING REQUIREMENTS

Chemical Fertilizer

Visual Inspection:  Provide the bag label, showing the guaranteed analysis.

NOTE:	The requirements are for pounds of nutrient (must be calculated) - not total pounds of fertilizer.  See subsection 816.04.C or per special provision.

Example of a 50 lbs bag of fertilizer “19-19-19” is 28.5 lbs of Nutrient.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

  - Engineer will pay based on measurements and calculations.

8160026		MULCH ANCHORING

Pg 1 of 1	Pay Unit:	Square Yard/Each

MATERIALS:	Mulch Anchoring - (Tackifier)

ACCEPTANCE TESTING REQUIREMENTS

Mulch Anchoring - (Tackifier)

- VI and must be on Qualified Products List (917.15C5).

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will pay based on measurements and calculations.

8160027 - 8160028	MULCH BLANKET___

Pg 1 of 1	Pay Unit:	Square Yard

MATERIALS:	High Velocity Mulch Blankets, Mulch Blanket,

ACCEPTANCE TESTING REQUIREMENTS

High Velocity Mulch Blankets

- VI and must be on Qualified Products List (917.15B1).

Mulch Blankets

- VI and must be on Qualified Products List (917.15B2).

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Refer to Standard Plan R-100

- Measurement and payment

- Engineer will pay based on measurements and calculations and includes providing, placing and anchoring.

8160035 – 8160045	SEEDING, MIXTURE __

Pg 1 of 1	Pay Unit:	Pound

MATERIALS:	Seed Mixture

ACCEPTANCE TESTING REQUIREMENTS

Seed Mixture

- All Projects with 5 acres or more of restoration, tests are required if the Grass Seed Testing Special Provision is included in the Contract.

Grass Seed Varieties:

VI and must be on Qualified Product list

Visual Inspection:  Maximum 1100 pounds.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Date on seed ticket not to exceed of one year

NOTE:	Computations must be shown on IDR using rates of application as shown in the spec book or proposal.

- Measurement and payment

- Engineer will pay based on pounds of seed applied.

8160100 - 8160103	SLOPE RESTORATION, _____

Pg 1 of 2	Pay Unit:	Square Yard

MATERIALS:	Fertilizer, Herbicides, High Velocity Mulch Blanket, Mulch, Mulch Anchoring, Mulch Blanket, Permanent Turf Reinforcement Mat (TRM), Seed Mixture, Sod, Pegs for Sodding, Top soil

ACCEPTANCE TESTING REQUIREMENTS

Fertilizer

Visual Inspection:  Provide the bag label, showing the guaranteed analysis.

Herbicides

- A Test Data Certification.

High Velocity Mulch Blankets

- VI and must be on Qualified Products List (917.15B1).

Mulch

- VI

Mulch Anchoring Material

- VI and must be on Qualified Products List (917.15C5).

Mulch Blankets

- VI and must be on Qualified Products List (917.15B2).

Permanent Turf Reinforcement Mat (TRM)

- Must meet Special Provision Requirements

Seed Mixture

- All Projects with 5 acres or more of restoration, tests are required if the Grass Seed Testing Special Provision is included in the Contract.

Grass Seed Varieties:

VI and must be on Qualified Product list

Visual Inspection:  Maximum 1100 pounds.

Sod

Visual Inspection:  All material placed.

8160100 - 8160103	SLOPE RESTORATION, _____

Pg 2 of 2

Pegs for Sodding

Visual Inspection:  All material placed.

Top Soil

Visual Inspection:  	All material placed.  Per section 917.07 of the Standard Specification

for Construction.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Verify topsoil depths.

Note: Refer to Standard Plan R-100

NOTE:	Computations must be shown on IDR using rates of application as shown in the spec book or proposal.

The requirements are for pounds of nutrient (must be calculated) - not total pounds of fertilizer.  See subsection 816.04.C or per special provision.

Example of a 50 lbs bag of fertilizer “19-19-19” is 28.5 lbs of Nutrient.

- Measurement and payment

- Engineer will pay based on measured Syd in place.

8160055	SODDING

Pg 1 of 1	Pay Unit:	Square Yard

MATERIALS:	Sod, Pegs for Sodding

ACCEPTANCE TESTING CRITERIA

Sod

Visual Inspection:  All material placed.

Pegs for Sodding

Visual Inspection:  All material placed.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will pay based on measured Syd in place.

8190330 – 8190346	LUMINAIRE

Pg 1 of 1	Pay Unit:	Each

MATERIALS:	Luminaire

ACCEPTANCE TESTING REQUIREMENTS

Luminaire

- A General Certification.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

- Measurement and payment

- Engineer will pay based on each placed.

8230150 – 8230181	WATER MAIN

Pg 1 of 2	Pay Unit:	Foot

MATERIALS:	Ductile Iron Pipe, Granular Cl III and Granular Cl IIIA

ACCEPTANCE TESTING REQUIREMENTS

Ductile Iron Pipe

- A General Certification.

Visual Inspection:  Maximum 250 feet.

Granular Materials

Prequalified Sources:

- One ticket REQUIRED per load containing the following data.

- MDOT aggregate source number (Pit Number)

- Date of shipment

- Time of shipment (if applicable)

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number (if applicable)

2.	Documentation verifying passing QA test results in project files, see Materials Quality Assurance Procedures Manual  Section 7.

3.	See Procedures for Aggregate Inspection Manual for reduced acceptance testing requirements if material is from a pre-qualified supplier.

4.	In addition, the following statement shall be printed or stamped on each ticket: “I attest that aggregate as delivered from this pre-qualified source meets specification requirements for the listed Michigan series and class for quantity stated.
Date __________________    Signature _________________________________.
This statement must be signed by an authorized company representative.  This statement does not signify acceptance by MDOT of the aggregate.

Non-Prequalified Sources:

- One ticket REQUIRED per load containing the following data if applicable

- MDOT aggregate source number

- Date and time of shipment

- MDOT control section and job number

- Michigan series number and class letter of aggregate

- Weight or volume shipped

- Suppliers name, telephone number and location

- Truck identifier number

- Test reports must be in project files

- Class II - One test per 3,000 cubic yards.

- Class III or IIIA One test per 10,000 cubic yards.

8230150 – 8230181	WATER MAIN

Pg 2 of 2

Visual Inspection:

Class III – Maximum 500 cubic yards per project.

Class III A – Maximum 100 cubic yards per project

NOTE:

Check for the Buy America compliance on all steel and iron certifications which is required on Federal Aid Projects.  All permanently incorporated steel or iron materials must be melted and all manufacturing processes including the coating must occur in the coating must occur in the United States.  It should be noted that this is different than the “Buy American” statement which may also be listed.  “Buy American” is not an acceptable alternate to “Buy America”.  See the MDOT Construction WIKI section 105.10

INDEPENDENT ASSURANCE TESTING (I.A.T.) REQUIREMENTS

1.	See Notes page for IAT requirements.

CONSTRUCTION

1.	Inspector’s Daily Report

- IDR shall show the inspector’s computations, measurements and supporting documentation verifying quantity submitted for pay.

- All materials used must be VI and accepted by the inspector with notation on the IDR.

Note: Standard Plans R-83

- Measurement and payment

- Engineer will pay based on measurements along the centerline of the pipe with no deductions for fittings.

- Density Reports

- Review reports to see that all test and retests meet MDOT requirements 
(see form 0582B).

- All density reports are to be placed in ProjectWise on a weekly basis as a minimum.

END OF DATE FIVE and SEVEN

# Text boxes

DOCUMENTATION GUIDE

(Minimum Documentation Requirements for Pay Item Approvals and Material Acceptance)

2019 EDITION

VERSION 2.0

December 1, 2018

CONSTRUCTION FIELD SERVICES DIVISION

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents

Go To

Table of Contents